## Slide 1: Inverse Geochemical Modeling: Principles, Application & Examples
Pierre Glynn
March 2011

## Slide 3: Principles
Objective: Describe the chemical and isotopic evolution observed on a hydrologic flow path in terms of sets (models) of balanced reactions.
Input:
  Analytical data for one (or more if mixing occurs) “initial” solutions and one “final” solution
  Stoichiometry of plausible reactants and products
Output:
  Mass-balance models – heterogeneous reactive mass transfers (mineral/gas dissolution/exsolution, sorption/exchange) that account for changes in chemistry and isotopic composition.

## Slide 4
Fundamental principles used:
  Elemental mass balance and valence state balance (PHREEQC)
  Isotope mass balance
  Redox State (NETPATH) or electron balance (PHREEQC)
  Solution charge balances
  Solution/phase adjustment constraints within specified uncertainty levels (elements, pH, isotopes)
  Alkalinity balance (& solution charge imbalance acct.)
  Water balance

## Slide 5: Equations solved in PHREEQC
Generalized mole-balance:
Alkalinity balance:
And when alklalinity has not been measured:
c: stoichiometric coefficients; α: mass transfer amounts: T: number of moles in a solution; δ: error adjustments
q: solutions; Q: final solution; r: redox reactions; p: phases; i: species; m: element or valence state

## Slide 6
Electron balance:
Solution charge balance:
where Tz,q is the charge imbalance in a solution determined from an aqueous-speciation calculation and zmtot is the sum of the charge on the master species for an element or valence state plus the alkalinity assigned to the master species:
Inequality constraints (um,q: specified uncertainties):
        Potentially:

## Slide 7
Water balance:
Isotope balance:
Ri are isotopic ratios or contents of elements in aqueous solution or in phases. PHREEQC neglects the products of δ adjustments in its calculations, given that the adjustments are expected to be small.
Isotope adjustment constraints:

## Slide 8
Algorithm developed by Barrodale and Roberts (1980) solves the sets of linear equality and inequality constraints using a minimization technique.
The unknowns solved for are: mixing fractions, phase and redox mass transfers, and element/valence/isotope adjustments.

## Slide 9: Application requirements (#1)
Hydrological connection (initial and final waters used are representative of evolution on a given flow-path).
Hydrological direction: final water represents initial water(s) after reactions.
Hydrologic “mixing” proposed is representative of either dispersive mixing along a flow path, or waters pumped in from different ground-water zones (aquifers, aquitards, lenses…), or from a combination of ground-water and surface-water bodies (lakes, rivers, ocean), or from mixing induced inside the well or by flow on the outside of the well casing.

## Slide 11: Application requirements (#2)
Thermodynamic feasibility: reactions proposed are thermodynamically feasible (given SI values and thermodynamic potentials). Speciation calculations are needed to establish SI and reaction potentials.
Kinetic feasibility: reaction amounts determined in the inverse models are realistic of field reaction rates, given estimated hydrologic travel times.

## Slide 12
For a first order reaction A ↔ B:

## Slide 13: Application requirements (#3)
Mineralogical feasibility: Mineral/gas dissolution reactions proposed are feasible because the occurrence and exposure of the waters to the minerals/gases is likely. Proposed exchange/sorption reactions are feasible because the initial exchange/sorption surfaces present are realistic and likely to behave according to modeled selectivities (eg. Ca uptake/Na release).

## Slide 14: Mineralogical Determinations
Thin Sections or ion microprobe or Scanning Electron Microscope with Energy Dispersive X-rays
  Mineralogy and composition of specific minerals.
  Poor job of fine grained secondary phases such as clays and oxy-hydroxides
X-ray diffraction
  Gives mineralogy, including fine grained phases and clays.
  Does not give the specific mineral compositions.
  Quantitation techniques are improving
Knowledge of geologic framework, geochemistry and hydrology

## Slide 15: Application requirements (#4)
Steady-state requirements, or proper accounting of chemical/hydrologic transience.
  Can be problem due to synoptic sampling of wells.
  Hydrologic steady-state is established for the evolution/transit time represented by the sampled waters. Alternatively, initial and final waters are sampled at different times and chosen to ensure hydrologic connection/direction.
  Chemical steady-state, or reaction fronts/zones between initial and final wells have not moved past the final well in the transit time represented by the hydrologic flow path.

## Slide 16: Examples and Problems

## Slide 17: “Pen & paper” problem
Two waters:
  Recharge water #1 is pure. Final water (#2) is from a well and has total Ca and total inorganic C concentrations of 8.3 and 16.0 mmol/L.
  Hypothesized reacting phases are Calcite (CaCO3) and carbon dioxide (CO2).
  What are the equations to solve? How much calcite and CO2 is predicted to dissolve to make up water #2 from water #1?
Answers provided in “Inverse Modeling with PHREQC.doc” file.

## Slide 18: PHREEQC Inverse modeling

## Slide 19: INVERSE Keyword
Options:
  -solutions - define initial solution(s) and final solution numbers.
  -phases – list of possible reactants (already defined with PHASES or EXCHANGE_SPECIES keywords) with associated dissolution or precipitation constraints and isotopic uncertainties.
  -uncertainties - global uncertainties for all elements in each solution.
  -balances - (1) force a mole balance for elements not in phases; (2) uncertainties that differ from global uncertainties.
  -isotopes – force an isotope balance on selected isotopes given provided uncertainties (usually in per mil or % modern C) for each solution.

## Slide 20
Other options:
  -minimal - models for which no phase can be removed, i.e. for which no mineral/solution subset can be found, by further solution adjustments.
  -range - maximum and minimum mole transfers obtained by varying elemental and/or isotopic adjustments within the uncertainty limits.
  -force_solutions – forces one or more solution to be included in all range calculations.
  -mineral_water – includes (default) or excludes water derived from minerals in the water balance equation.
  -uncertainty_water – allows an uncertainty term for the water balance equation (default is 0).
  -tolerance – used to adjust tolerance for optimizing solver. Larger value (than 10-10) needed only in case of very large mole transfers (> 1000 moles).

## Slide 21: PHREEQC walk-through problem
Analyses | Initial well | Final well
pH | 7.4 | 7.2
pe | 4.0 | -3.8
Ca (mmol/kg H2O) | 1.2 | 2.3
Mg (mmol/kg H2O) | 0.9 | 1.7
SO4 (mmol/kg H2O) | 0.0 | 1.7
Alkalinity (mmol/kg H2O) | 4.1 | 4.5
Total S2- (mmol/kg H2O) | - | 0.25
TDIC (mmol/kg H2O) | 4.4 | 4.8

## Slide 22
Saturation Indices/Partial Pressures | Initial well | Final well
Calcite | 0.04 | 0.04
Dolomite | 0.09 | 0.07
Gypsum |  | -1.38
pCO2 | -2.01 | -1.81
Assume calcite (CaCO3), dolomite (CaMg(CO3)2, gypsum (CaSO4.2H2O), organic matter (CH2O), and carbon dioxide (CO2) are reactant phases.
You need a SOLUTION keyword for the initial and the final solutions; an INVERSE_MODELING keyword; and a PHASES keyword to define CH2O, which is not in the default database files.

## Slide 23
SOLUTION - enter pe, pH, and concentration data for each element and element redox state.
INVERSE_MODELING - enter information for -solutions, -phases, and -uncertainties (0.05), -range.
PHASES - Use the following equation for the dissociation of CH2O:
  CH2O = 0.5CH4 + 0.5CO2. Set log K arbitrarily.
Why is the value of log K for a phase reaction irrelevant in an inverse modeling problem?

## Slide 24
SOLUTION 1
pH 7.4
pe 4.0
Ca 1.2
Mg 0.9
S(6) 0.0
S(-2) 0.0
C(4) 4.4
SOLUTION 2
pH 7.2
pe -3.8
Ca 2.3
Mg 1.7
S(6) 1.7
S(-2) .25
C(4) 4.8
INVERSE_MODELING
-solutions 1 2
-phases
Calcite
Dolomite
Gypsum
CH2O
CO2(g)
-uncertainty 0.05
-range
PHASES
CH2O
CH2O = 0.5CO2 + 0.5CH4
log_k 0
END
Walk-through problem
input file
Output provided in “Inverse Modeling with PHREQC.doc” file.

## Slide 25
Sierra Nevada problem
From Garrels and Mackenzie, 1967:
“Origin of the chemical compositions of some springs and lakes”
Ephemeral and Perennial Spring analyses from Feth et al. (1964)
Garrels and Mckenzie performed a “reverse” mass balance
reconstituting the original granitic rock from the difference in
water composition.

## Slide 26
Sierra Nevada Spring Compositions
Ephemeral
Spring
Perennial
Spring

## Slide 27: Garrels & Mackenzie solution
"Halite"
NaCl
"Gypsum"
CaSO4
CO2 gas
CO2
Calcite
CaCO3
Silica
SiO2
Biotite
KMg3AlSi3O10(OH)2
Plagioclase An38
Na0.62Ca0.38Al1.38Si2.62O8
Kaolinite
Al2Si2O5(OH)4
Ca-Montmorillonite
Ca0.17Al2.33Si3.67O10(OH)2
.016
.015
.427
.115
0
.014
.175
-.033
-.081
mass transfers
(mmol/kg water)

## Slide 28
SOLUTION 1 Ephemeral Springs
temp 25
pH 6.2
pe 4
redox pe
units mmol/kgw
density 1
Ca 0.078
Cl 0.014
K 0.028
Mg 0.029
Na 0.134
S(6) 0.01
Si 0.273
Alkalinity 0.328
-water 1 # kg
SOLUTION 2 Perennial Springs
temp 25
pH 6.8
pe 4
redox pe
units mmol/kgw
density 1
Ca 0.41
Cl 0.03
K 0.04
Mg 0.071
Na 0.259
S(6) 0.025
Si 0.41
Alkalinity 0.895
-water 1 # kg

## Slide 32
Always written as dissolution

## Slide 34
Try running the Sierra Nevada problem initially with all uncertainties set to 0.05 (5% or ± 0.05 for pH).
  How many models did you find?
  Are the models reasonable?
  What are the phases common to all three models?
  What are the ones that differ?
Try running the same problem but change the global uncertainties to 0.025, while keeping the uncertainty on Ca in the initial solution set at 0.05.
  How many models did you find?
Could you construct a model that did not require dissolution of halite? Or dissolution of gypsum?

## Slide 35
Three possible models found (only first two if Ca uncertainty is set 0.05 for the initial solution) :
  #1 has kaolinite and chalcedony
  #2 has kaolinite and Ca-montmorillonite
  #3 has Ca-montmorillonite and chalcedony
The common phases in all models are:
  biotite, plagioclase, calcite, CO2, gypsum, halite.

## Slide 36: SOLUTION 1 Ephemeral Springs temp 25 pH 6.2 pe 4 redox pe units mmol/kgw density 1 Ca 0.078 Cl 0.014 K 0.028 Mg 0.029 Na 0.134 S(6) 0.01 Si 0.273 Alkalinity 0.328 -water 1 # kg SOLUTION 3 Precipitation temp 25 pH 5.8 pe 4 redox pe units umol/l density 1 Na 0.11 Ca 0.068 Mg 0.022 K 0.02 S(6) 0.01 Cl 0.013 Si 0.27 Alkalinity 0.314 -water 1 # kg
INVERSE_MODELING 1 -solutions 3 1 -uncertainty 0.05 0.05 -phases Kaolinite Ca-Montmorillonite CO2(g) Plag(An38) SiO2(a) Gypsum K-feldspar Biotite -tolerance 1e-010 -mineral_water true PHASES Plag(An38) Na0.62Ca0.38Al1.38Si2.62O8 + 5.52H+ + 2.48H2O
= 1.38Al+3 + 0.38Ca+2 + 2.62H4SiO4 + 0.62Na+ log_k 0 Biotite KMg3AlSi3O10(OH)2 + 6H+ + 4H2O
= Al(OH)4- + 3H4SiO4 + K+ + 3Mg+2log_k 0 END
No halite or calcite.
Add K-feldspar.
Alex Blum’s solution
Problems with this solution: ignores Cl
and calcite is in fact a likely reactant!

## Slide 37
Phase mole transfers: Minimum Maximum
Kaolinite -4.796e-005 0.000e+000 0.000e+000 Al2Si2O5(OH)4
Ca-Montmorillon -9.511e-005 0.000e+000 0.000e+000 Ca0.165Al2.33Si3.67O10(OH)2
CO2(g) 7.739e-004 0.000e+000 0.000e+000 CO2
Plag(An38) 2.098e-004 0.000e+000 0.000e+000 Na0.62Ca0.38Al1.38Si2.62O8
SiO2(a) 8.404e-005 0.000e+000 0.000e+000 SiO2
Gypsum 9.990e-006 0.000e+000 0.000e+000 CaSO4:2H2O
K-feldspar 1.832e-005 0.000e+000 0.000e+000 KAlSi3O8
Biotite 9.659e-006 0.000e+000 0.000e+000 KMg3AlSi3O10(OH)2
No halite or calcite. How would you get these in the soil?
Add K-feldspar. That makes sense.
But….Gypsum? There is something we are missing with SO4

## Slide 38: Pinal Creek Problem
Detailed in Glynn and Brown (1996; MSA volume on “Reactive Transport Modeling”). Paper also contains an inverse modeling comparison of NETPATH vs. PHREEQC, and a reactive transport modeling study that makes use of the inverse modeling results.

## Slide 39
Webster lake: an artificial lake used to dump waste sulfuric acid between 1946 and 1986. The 25 km-long valley narrows northward and the basement comes up, pinching out the consolidated basin fill and unconsolidated alluvial sediments.
Carbonates, Mn-oxides, and a mix of mafic and felsic silicates and minerals are present in the sediments.

## Slide 40
Two contaminated waters and a background water which dilutes the contamination as it travels downgradient at ~5 m/day. pH front travels at 1/5th the speed.

## Slide 41
What is the Cl concentration between well 402 and the downgradient well 503?
How about the SO4?
What about the pH?
What about the Mn concentration?
What about the Fe concentration?
How about Al?

## Slide 43
Groundwater evolution:
  Do you have an explanation for the change in Cl and SO4?
  What are the processes controlling pH?
  What about the Mn and Fe controls?
  And the controls on Al?
Use the file “pinal-msa.pqi” to run the problem with a subset of the minerals/reactions considered in Glynn and Brown (1996).
  What are the differences in minerals considered?

## Slide 46: Tar Creek problem
Evolution of a recharge water during pyrite and sphalerite oxidation, carbonate, albite and halite dissolution.
Use file “tarcreek.pqi”

## Slide 47: Potomac Sulfate reduction
Reaction of a seawater with organic carbon, iron oxides, calcite, and exchange reactions.
Use file “v6.pqi”.

## Slide 48: Potomac Intense Methanogenesis
Ca/Mg/Na/K exchange, calcite dissolution, and reaction of an NH3-rich organic phase causing fermentation and methanogenesis.
Use file “v28.pqi”.

## Slide 49: Floridan Aquifer
Plummer and Sprinkle (HJ 2001). Evolution of ground water in a carbonate aquifer: anhydrite dissolution causes dedolomitization and secondary calcite precipitation, organic carbon oxidation causes sulfate reduction and pyrite precipitation.
No isotope data provided in file “florida-1-4.pqi”
Run the problem from wells 1.1 to 2.4 and comment.
Change the file and rerun for the evolution between wells 2.4 and 2.6. Comment.

## Slide 50: Madison Aquifer
Plummer et al. (WRR 1990) & Parkhurst (1997). Classic 14C dating study. Evolution of waters through a dedolomitization reaction sequence with anhydrite dissolution, Ca/Na exchange, halite & sylvite dissolution, pyrite precipitation, organic carbon oxidation…
13C, 34S data provided in file “madison.pqi”.
Run & comment. How does this problem differ from the Florida problem in term of reactions considered?

## Slide 51: Yucca Mountain perched waters
Shows an example of using PHREEQC to conduct inverse modeling to attempt to date ground waters using 14C and 13C isotopic data.
Data found in “inverse modeling with PHREEQC.doc” file.
Conduct inverse modeling on the SD-7 water assuming initial water is dilute rain water at equilibrium with atm. CO2.

## Slide 52: PHREEQC vs. NETPATH
Netpath strengths:
  Models Rayleigh isotopic fractionation, i.e. the isotopic evolution of a solution as various minerals dissolve into it and precipitate out of it.
  14C dating. Calculates a variety of classical 14C models (Vogel, Mook, Ingerson & Pearson, Tamers, Fontes, Eichinger) as well as its own inverse-model driven calculation.
  Highly flexible. Allows putting in components & phases gradually.

## Slide 53
PHREEQC strengths (compared to NETPATH)
  Solves for the solution charge balance and for a set of analytical adjustments that account for uncertainties in the input solution data
  Solves mole balance equations for:
    alkalinity balance
    Individual valence states of redox elements
    Water balance
  Forces consideration of all elements specified in the initial and final solution compositions and in the specified reaction phases.

## Slide 54: Madison Aq. Comparison NETPATH/PHREEQC “worst-case scenario” from Parkhurst (1997)
reaction | Netpath (charge balanced) | PHREEQC
Ca.75Md.25/Na2 exch. | 7.6 | 8.2
Dolomite diss. | 5.3 | 5.6
Calcite (precip.) | -12.3 | -12.3
Anhydrite diss. | 22.5 | 22.4
CH2O oxidation | 4.3 | 3.3
Halite | 15.8 | 15.3
13C final water | -4.3 | -2.9
Corrected 14C age | 12.5 K | 12.6K