## Slide 1: Monday
Thermodynamics of aqueous solutions
  Ion association
  Pitzer
  SIT
SOLUTION and SOLUTION _SPREAD
  Units
  pH—ratio of HCO3-/CO2
  pe—ratio of oxidized/reduced valence states
  Charge balance
  Phase boundaries
Saturation indices
  Uncertainties
  Useful minerals
Identify potential reactants
<number>
Notes: <number>

## Slide 2: Solution Definition and Speciation Calculations
Ca
Na
SO4
Mg
Fe
Cl
HCO3
Reactions
Saturation Indices
Speciation calculation
Inverse Modeling
Transport
<number>
Notes: <number>

## Slide 3
Constituent | Value
pH pe Temperature Ca Mg Na K Fe Alkalinity as HCO3 Cl SO4 | 8.22 8.45 25 412.3 1291.8 10768 399.1 .002 141.682 19353 2712
Seawater: Units are ppm
<number>
Notes: <number>
ppm, temperature independent
mg/L, temperature dependent
mg vs moles
Mol/kg water
Kgs ~ kgw
Density of seawater 1.02; Ppm ~ mg/L; mol/L ~ mol/kgw

## Slide 4: Initial Solution 1. Questions
What is the approximate molality of Ca?
What is the approximate alkalinity in meq/kgw?
What is the alkalinity concentration in mg/kgs as CaCO3?
What effect does density have on the calculated molality?
PHREEQC results are always moles or molality
<number>
Notes: <number>
IS.1. Questions
For most waters, we can assume most of the mass in solution is water. Mass of water in 1 kg seawater ~ 1 kg.
412/40 ~ 10 mmol/kgw
142/61 ~ 2.4 meq/kgw
2.4*50 ~ 120 mg/kgw as HCO3
None, density will only be used when concentration is specified as per liter.

## Slide 5: Initial Solution 1.
For most waters, we can assume most of the mass in solution is water. Mass of water in 1 kg seawater ~ 1 kg.
412/40 ~ 10 mmol/kgw ~ 0.01 molal
142/61 ~ 2.3 meq/kgw ~ 0.0023 molal
2.3*50 ~ 116 mg/kgw as CaCO3
None, density will only be used when concentration is specified as per liter.
<number>

## Slide 6: Solutions
Required for all PHREEQC calculations
SOLUTION and SOLUTION _SPREAD
  Units
  pH
  pe
  Charge balance
  Phase boundaries
Saturation indices
  Uncertainties
  Useful minerals
  Identify potential reactants
<number>
Notes: <number>

## Slide 7: Periodic_table.bmp
<number>

## Slide 8: Default Gram Formula Mass
Element/Redox State | Default “as” phreeqc.dat/wateq4f.dat
Alkalinity | CaCO3
C, C(4) | HCO3
CH4 | CH4
NO3- | N
NH4+ | N
Si | SiO2
PO4 | P
SO4 | SO4
Default GFW is defined in 4th field of SOLUTION_MASTER_SPECIES in database file.
<number>
Notes: <number>
SOLUTION_MASTER_SPECIES
#element species alk gfw_formula element_gfw
Ca Ca+2 0.0 Ca 40.08
C CO3-2 2.0 HCO3 12.0111
C(+4) CO3-2 2.0 HCO3
C(-4) CH4 0.0 CH4
Alkalinity CO3-2 1.0 Ca0.5(CO3)0.5 50.05

## Slide 9: Changing Database
Each time you run
Or
File->Properties
Set
  Input file
  Output file
  Database file
Also
Options->Set default database
<number>
Notes: <number>

## Slide 10: Databases
Ion association approach
  Phreeqc.dat—simplest (subset of Wateq4f.dat)
  Wateq4f.dat—more trace elements
  Minteq.dat—translated from minteq v 2
  Minteq.v4.dat—translated from minteq v 4
  Llnl.dat—most complete set of elements, temperature dependence
  Iso.dat—(in development) thermodynamics of isotopes
Pitzer specific interaction approach
  Pitzer.dat—Specific interaction model (many parameters)
SIT specific interaction theory
  Sit.dat—Simplified specific interaction model (1 parameter)
<number>

## Slide 11: PHREEQC Databases
Other data blocks related to speciation
SOLUTION_MASTER_SPECIES—Redox states and gram formula mass
SOLUTION_SPECIES—Reaction and log K
PHASES—Reaction and log K
<number>
Notes: <number>

## Slide 12: What is a speciation calculation?
Input:
  pH
  pe
  Concentrations
Equations:
  Mass-balance—sum of the calcium species = total calcium
  Mass-action—activities of products divided by reactants = constant
  Activity coefficients—function of ionic strength
Output
  Molalities, activities
  Saturation indices
<number>
Notes: <number>

## Slide 13: Mass-Balance Equations
Analyzed concentration of sulfate = (SO4-2) + (MgSO40) + (NaSO4-) + (CaSO40) + (KSO4-) + (HSO4-) + (CaHSO4+) + (FeSO4) + (FeSO4+) + (Fe(SO4)2-) + (FeHSO4+) + (FeHSO4+2)
() indicates molality
<number>

## Slide 14: Mass-Action Equations
Ca+2 + SO4-2 = CaSO40
[] indicates activity
<number>
Notes: <number>

## Slide 15: Activity
WATEQ activity coefficient
Davies activity coefficient
<number>
Notes: <number>

## Slide 16: Uncharged Species
<number>
bi, called the Setschenow coefficient
Value of 0.1 used in phreeqc.dat, wateq4f.dat.

## Slide 17: Pitzer Activity Coefficients
ma concentration of anion
mc concentration of cation
Ion specific parameters
F function of ionic strength, molalities of cations and anions
<number>

## Slide 18: SIT Activity Coefficients
mk concentrations of ion
<number>
Interaction parameter
A = 0.51, B = 1.5 at 25 C

## Slide 19: Aqueous Models
Ion association
  Pros
    Data for most elements (Al, Si)
    Redox
  Cons
    Ionic strength < 1
    Best only in Na, Cl medium
    Inconsistent thermodynamic data
    Temperature dependence
<number>

## Slide 20: Aqueous Models
<number>
Pitzer specific interaction
  Pros
    High ionic strength
    Thermodynamic consistency for mixtures of electrolytes
  Cons
    Limited elements
    Little if any redox
    Difficult to add elements
    Temperature dependence

## Slide 21: Aqueous Models
<number>
SIT
  Pros
    Better possibility for higher ionic strength than ion association
    Many fewer parameters
    Redox
    Actinides
  Cons
    Poor results for gypsum/NaCl in my limited testing
    Temperature dependence
    Consistency?

## Slide 22: PhreeqcI: SOLUTION Data Block
<number>
Notes: <number>

## Slide 23: Number, pH, pe, Temperature
<number>
Notes: <number>

## Slide 24: Solution Composition
Set units!
Default is mmol/kgw
Click when done
Set concentrations
“As”, special units
Select elements
<number>
Notes: <number>

## Slide 25: Run Speciation Calculation
Run
Select files
<number>
Notes: <number>

## Slide 26: Ion Association Model Results
<number>
Notes: <number>
------------------
Reading data base.
------------------
SOLUTION_MASTER_SPECIES
SOLUTION_SPECIES
PHASES
EXCHANGE_MASTER_SPECIES
EXCHANGE_SPECIES
SURFACE_MASTER_SPECIES
SURFACE_SPECIES
RATES
END
------------------------------------
Reading input data for simulation 1.
------------------------------------
DATABASE C:\Program Files\USGS\Phreeqc Interactive 2.16.0\phreeqd.dat
SOLUTION 1
temp 25
pH 8.22
pe 8.45
redox pe
units ppm
density 1
Ca 412.3
Mg 1291.8
Na 10768
K 399.1
Fe 0.002
Alkalinity 141.682 as HCO3
Cl 19353
S(6) 2712
water 1 # kg
-------------------------------------------
Beginning of initial solution calculations.
-------------------------------------------
Initial solution 1.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Alkalinity 2.406e-003 2.406e-003
Ca 1.066e-002 1.066e-002
Cl 5.657e-001 5.657e-001
Fe 3.711e-008 3.711e-008
K 1.058e-002 1.058e-002
Mg 5.507e-002 5.507e-002
Na 4.854e-001 4.854e-001
S(6) 2.926e-002 2.926e-002
----------------------------Description of solution----------------------------
pH = 8.220
pe = 8.450
Specific Conductance (uS/cm, 25 oC) = 52808
Density (g/cm3) = 1.02328
Activity of water = 0.981
Ionic strength = 6.748e-001
Mass of water (kg) = 1.000e+000
Total carbon (mol/kg) = 2.182e-003
Total CO2 (mol/kg) = 2.182e-003
Temperature (deg C) = 25.000
Electrical balance (eq) = 7.967e-004
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 0.07
Iterations = 7
Total H = 1.110144e+002
Total O = 5.562980e+001
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 2.674e-006 1.629e-006 -5.573 -5.788 -0.215
H+ 7.981e-009 6.026e-009 -8.098 -8.220 -0.122
H2O 5.551e+001 9.806e-001 1.744 -0.009 0.000
C(4) 2.182e-003
HCO3- 1.516e-003 1.024e-003 -2.819 -2.990 -0.170
MgHCO3+ 2.198e-004 1.642e-004 -3.658 -3.785 -0.127
NaHCO3 1.669e-004 1.950e-004 -3.777 -3.710 0.067
MgCO3 8.924e-005 1.042e-004 -4.049 -3.982 0.067
NaCO3- 6.726e-005 5.026e-005 -4.172 -4.299 -0.127
CaHCO3+ 4.603e-005 3.110e-005 -4.337 -4.507 -0.170
CO3-2 3.826e-005 7.969e-006 -4.417 -5.099 -0.681
CaCO3 2.728e-005 3.187e-005 -4.564 -4.497 0.067
CO2 1.211e-005 1.415e-005 -4.917 -4.849 0.067
FeCO3 1.700e-016 1.985e-016 -15.770 -15.702 0.067
FeHCO3+ 1.423e-016 1.063e-016 -15.847 -15.973 -0.127
Ca 1.066e-002
Ca+2 9.504e-003 2.380e-003 -2.022 -2.623 -0.601
CaSO4 1.083e-003 1.265e-003 -2.965 -2.898 0.067
CaHCO3+ 4.603e-005 3.110e-005 -4.337 -4.507 -0.170
CaCO3 2.728e-005 3.187e-005 -4.564 -4.497 0.067
CaOH+ 8.604e-008 6.429e-008 -7.065 -7.192 -0.127
CaHSO4+ 5.979e-011 4.467e-011 -10.223 -10.350 -0.127
Cl 5.657e-001
Cl- 5.657e-001 3.528e-001 -0.247 -0.452 -0.205
FeCl+ 6.769e-016 5.058e-016 -15.169 -15.296 -0.127
FeCl+2 9.556e-019 2.978e-019 -18.020 -18.526 -0.506
FeCl2+ 6.281e-019 4.693e-019 -18.202 -18.329 -0.127
FeCl3 1.417e-020 1.656e-020 -19.849 -19.781 0.067
Fe(2) 6.007e-015
Fe+2 4.525e-015 1.039e-015 -14.344 -14.984 -0.639
FeCl+ 6.769e-016 5.058e-016 -15.169 -15.296 -0.127
FeSO4 4.213e-016 4.921e-016 -15.375 -15.308 0.067
FeCO3 1.700e-016 1.985e-016 -15.770 -15.702 0.067
FeHCO3+ 1.423e-016 1.063e-016 -15.847 -15.973 -0.127
FeOH+ 7.153e-017 5.345e-017 -16.145 -16.272 -0.127
FeHSO4+ 2.609e-023 1.949e-023 -22.584 -22.710 -0.127
Fe(3) 3.711e-008
Fe(OH)3 2.840e-008 3.318e-008 -7.547 -7.479 0.067
Fe(OH)4- 6.591e-009 4.924e-009 -8.181 -8.308 -0.127
Fe(OH)2+ 2.118e-009 1.583e-009 -8.674 -8.801 -0.127
FeOH+2 9.425e-014 2.937e-014 -13.026 -13.532 -0.506
FeSO4+ 1.093e-018 8.167e-019 -17.961 -18.088 -0.127
FeCl+2 9.556e-019 2.978e-019 -18.020 -18.526 -0.506
FeCl2+ 6.281e-019 4.693e-019 -18.202 -18.329 -0.127
Fe+3 3.509e-019 2.795e-020 -18.455 -19.554 -1.099
Fe(SO4)2- 6.371e-020 4.761e-020 -19.196 -19.322 -0.127
FeCl3 1.417e-020 1.656e-020 -19.849 -19.781 0.067
Fe2(OH)2+4 2.462e-024 2.322e-026 -23.609 -25.634 -2.025
FeHSO4+2 4.228e-026 1.318e-026 -25.374 -25.880 -0.506
Fe3(OH)4+5 1.122e-029 7.678e-033 -28.950 -32.115 -3.165
H(0) 5.540e-037
H2 2.770e-037 3.236e-037 -36.557 -36.490 0.067
K 1.058e-002
K+ 1.041e-002 6.495e-003 -1.982 -2.187 -0.205
KSO4- 1.627e-004 1.216e-004 -3.789 -3.915 -0.127
KOH 3.137e-009 3.665e-009 -8.503 -8.436 0.067
Mg 5.507e-002
Mg+2 4.742e-002 1.371e-002 -1.324 -1.863 -0.539
MgSO4 7.330e-003 8.562e-003 -2.135 -2.067 0.067
MgHCO3+ 2.198e-004 1.642e-004 -3.658 -3.785 -0.127
MgCO3 8.924e-005 1.042e-004 -4.049 -3.982 0.067
MgOH+ 1.084e-005 8.100e-006 -4.965 -5.092 -0.127
Na 4.854e-001
Na+ 4.791e-001 3.387e-001 -0.320 -0.470 -0.151
NaSO4- 6.053e-003 4.523e-003 -2.218 -2.345 -0.127
NaHCO3 1.669e-004 1.950e-004 -3.777 -3.710 0.067
NaCO3- 6.726e-005 5.026e-005 -4.172 -4.299 -0.127
NaOH 3.117e-007 3.641e-007 -6.506 -6.439 0.067
O(0) 6.554e-020
O2 3.277e-020 3.828e-020 -19.485 -19.417 0.067
S(6) 2.926e-002
SO4-2 1.463e-002 2.664e-003 -1.835 -2.574 -0.740
MgSO4 7.330e-003 8.562e-003 -2.135 -2.067 0.067
NaSO4- 6.053e-003 4.523e-003 -2.218 -2.345 -0.127
CaSO4 1.083e-003 1.265e-003 -2.965 -2.898 0.067
KSO4- 1.627e-004 1.216e-004 -3.789 -3.915 -0.127
HSO4- 2.089e-009 1.561e-009 -8.680 -8.807 -0.127
CaHSO4+ 5.979e-011 4.467e-011 -10.223 -10.350 -0.127
FeSO4 4.213e-016 4.921e-016 -15.375 -15.308 0.067
FeSO4+ 1.093e-018 8.167e-019 -17.961 -18.088 -0.127
Fe(SO4)2- 6.371e-020 4.761e-020 -19.196 -19.322 -0.127
FeHSO4+ 2.609e-023 1.949e-023 -22.584 -22.710 -0.127
FeHSO4+2 4.228e-026 1.318e-026 -25.374 -25.880 -0.506
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Anhydrite -0.84 -5.20 -4.36 CaSO4
Aragonite 0.61 -7.72 -8.34 CaCO3
Calcite 0.76 -7.72 -8.48 CaCO3
CO2(g) -3.38 -4.85 -1.47 CO2
Dolomite 2.41 -14.68 -17.09 CaMg(CO3)2
Fe(OH)3(a) 0.19 5.08 4.89 Fe(OH)3
Goethite 6.09 5.09 -1.00 FeOOH
Gypsum -0.63 -5.21 -4.58 CaSO4:2H2O
H2(g) -33.30 9.70 43.00 H2
H2O(g) -1.51 -0.01 1.51 H2O
Halite -2.50 -0.92 1.58 NaCl
Hematite 14.20 10.19 -4.01 Fe2O3
Jarosite-K -7.52 -16.73 -9.21 KFe3(SO4)2(OH)6
Melanterite -15.41 -17.62 -2.21 FeSO4:7H2O
O2(g) -16.52 -19.42 -2.89 O2
Siderite -9.19 -20.08 -10.89 FeCO3
------------------
End of simulation.
------------------
------------------------------------
Reading input data for simulation 2.
------------------------------------
-----------
End of run.
-----------

## Slide 27: Initial Solution 2. Exercise
Use phreeqc.dat to run a speciation calculation for seawater
Use pitzer.dat
Copy input to a new buffer
  Ctrl-a (select all)
  Ctrl-c (copy)
  File->new or ctrl-n
  (new input file)
  Ctrl-v (paste)
Constituent | Value
pH pE Temperature Ca Mg Na K Fe Alkalinity as HCO3 Cl SO4 | 8.22 8.45 25 412.3 1291.8 10768 399.1 .002 141.682 19353 2712
Units are ppm
<number>
Notes: <number>
# IS.2 Seawater
SOLUTION 1
temp 25
pH 8.22
pe 8.45
redox pe
units ppm
density 1
Ca 412.3
Mg 1291.8
Na 10768
K 399.1
Fe 0.002
Alkalinity 141.682 as HCO3
Cl 19353
S(6) 2712
-water 1 # kg

## Slide 28: Results of 2 Speciation Calculations
Tile
<number>
Notes: <number>
------------------
Reading data base.
------------------
SOLUTION_MASTER_SPECIES
SOLUTION_SPECIES
PHASES
PITZER
EXCHANGE_MASTER_SPECIES
EXCHANGE_SPECIES
SURFACE_MASTER_SPECIES
SURFACE_SPECIES
END
------------------------------------
Reading input data for simulation 1.
------------------------------------
DATABASE C:\Program Files\USGS\Phreeqc Interactive 2.16.0\pitzer.dat
SOLUTION 1
temp 25
pH 8.22
pe 8.45
redox pe
units ppm
density 1
Ca 412.3
Mg 1291.8
Na 10768
K 399.1
Fe 0.002
Alkalinity 141.682 as HCO3
Cl 19353
S(6) 2712
water 1 # kg
-------------------------------------------
Beginning of initial solution calculations.
-------------------------------------------
Initial solution 1.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Alkalinity 2.406e-003 2.406e-003
Ca 1.066e-002 1.066e-002
Cl 5.657e-001 5.657e-001
Fe 3.711e-008 3.711e-008
K 1.058e-002 1.058e-002
Mg 5.508e-002 5.508e-002
Na 4.854e-001 4.854e-001
S(6) 2.926e-002 2.926e-002
----------------------------Description of solution----------------------------
pH = 8.220
pe = 8.450
Density (g/cm3) = 0.99705
Activity of water = 0.981
Ionic strength = 7.218e-001
Mass of water (kg) = 1.000e+000
Total carbon (mol/kg) = 2.190e-003
Total CO2 (mol/kg) = 2.190e-003
Temperature (deg C) = 25.000
Electrical balance (eq) = 8.294e-004
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 0.07
Iterations = 14
Gamma iterations = 3
Osmotic coefficient = 0.90342
Density of water = 0.99706
Total H = 1.110144e+002
Total O = 5.562981e+001
----------------------------Distribution of species----------------------------
MacInnes MacInnes
MacInnes Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 3.150e-006 1.636e-006 -5.502 -5.786 -0.285
H+ 7.414e-009 6.026e-009 -8.130 -8.220 -0.090
H2O 5.551e+001 9.813e-001 1.744 -0.008 0.000
C(4) 2.190e-003
HCO3- 1.956e-003 1.067e-003 -2.709 -2.972 -0.263
CO3-2 9.885e-005 8.109e-006 -4.005 -5.091 -1.086
MgCO3 9.495e-005 9.495e-005 -4.023 -4.023 0.000
CaCO3 2.809e-005 2.809e-005 -4.551 -4.551 0.000
CO2 1.261e-005 1.425e-005 -4.899 -4.846 0.053
Ca 1.066e-002
Ca+2 1.063e-002 2.445e-003 -1.973 -2.612 -0.638
CaCO3 2.809e-005 2.809e-005 -4.551 -4.551 0.000
Cl 5.657e-001
Cl- 5.657e-001 3.524e-001 -0.247 -0.453 -0.206
Fe 3.711e-008
Fe+2 3.711e-008 7.959e-009 -7.430 -8.099 -0.669
K 1.058e-002
K+ 1.058e-002 6.889e-003 -1.976 -2.162 -0.186
Mg 5.508e-002
Mg+2 5.498e-002 1.382e-002 -1.260 -1.860 -0.600
MgCO3 9.495e-005 9.495e-005 -4.023 -4.023 0.000
MgOH+ 3.593e-006 3.493e-006 -5.444 -5.457 -0.012
Na 4.854e-001
Na+ 4.854e-001 3.426e-001 -0.314 -0.465 -0.151
S(6) 2.926e-002
SO4-2 2.926e-002 2.534e-003 -1.534 -2.596 -1.062
HSO4- 2.281e-009 1.455e-009 -8.642 -8.837 -0.195
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Anhydrite -0.85 -5.21 -4.36 CaSO4
Aragonite 0.52 -7.70 -8.22 CaCO3
Arcanite -5.14 -6.92 -1.78 K2SO4
Bischofite -7.27 -2.81 4.46 MgCl2:6H2O
Bloedite -5.67 -8.02 -2.35 Na2Mg(SO4)2:4H2O
Brucite -2.55 -13.43 -10.88 Mg(OH)2
Burkeite -12.30 -13.08 -0.77 Na6CO3(SO4)2
Calcite 0.70 -7.70 -8.41 CaCO3
Carnallite -9.76 -5.43 4.33 KMgCl3:6H2O
CO2(g) -3.38 -4.85 -1.47 CO2
Dolomite 2.43 -14.65 -17.08 CaMg(CO3)2
Epsomite -2.63 -4.51 -1.88 MgSO4:7H2O
Gaylussite -4.34 -13.77 -9.42 CaNa2(CO3)2:5H2O
Glaserite -8.34 -12.14 -3.80 NaK3(SO4)2
Glauberite -3.49 -8.73 -5.25 Na2Ca(SO4)2
Gypsum -0.64 -5.22 -4.58 CaSO4:2H2O
H2O(g) -1.52 -0.01 1.51 H2O
Halite -2.49 -0.92 1.57 NaCl
Hexahydrite -2.87 -4.50 -1.63 MgSO4:6H2O
Kainite -6.90 -7.10 -0.19 KMgClSO4:3H2O
Kalicinite -5.41 -15.47 -10.06 KHCO3
Kieserite -4.34 -4.46 -0.12 MgSO4:H2O
Labile_S -6.61 -12.28 -5.67 Na4Ca(SO4)3:2H2O
Leonhardite -3.60 -4.49 -0.89 MgSO4:4H2O
Leonite -7.43 -11.41 -3.98 K2Mg(SO4)2:4H2O
Magnesite 0.88 -6.95 -7.83 MgCO3
Mirabilite -2.40 -3.61 -1.21 Na2SO4:10H2O
Misenite -73.98 -84.79 -10.81 K8H6(SO4)7
Nahcolite -3.03 -13.78 -10.74 NaHCO3
Natron -5.28 -6.10 -0.82 Na2CO3:10H2O
Nesquehonite -1.81 -6.98 -5.17 MgCO3:3H2O
Pentahydrite -3.21 -4.50 -1.28 MgSO4:5H2O
Pirssonite -4.51 -13.74 -9.23 Na2Ca(CO3)2:2H2O
Polyhalite -8.06 -21.81 -13.74 K2MgCa2(SO4)4:2H2O
Portlandite -8.99 -14.18 -5.19 Ca(OH)2
Schoenite -7.10 -11.42 -4.33 K2Mg(SO4)2:6H2O
Sylvite -3.51 -2.61 0.90 KCl
Syngenite -4.69 -12.14 -7.45 K2Ca(SO4)2:H2O
Trona -8.43 -19.81 -11.38 Na3H(CO3)2:2H2O
------------------
End of simulation.
------------------
------------------------------------
Reading input data for simulation 2.
------------------------------------
-----------
End of run.
-----------

## Slide 29: Initial Solution 2. Questions
Write the mass-balance equation for calcium in seawater for each database.
What fraction of the total is Ca+2 ion for each database?
What fraction of the total is Fe+3 ion for each database?
What are the log activity and log activity coefficient of CO3-2 for each database?
What is the saturation index of calcite for each database?
<number>
Notes: <number>
() indicates molality
1a. Ca(total)= 1.066e-2 = (Ca+2) + (CaSO4) + (CaHCO3+) + (CaCO3) + (CaOH+) + (CaHSO4+)
1b. Ca(total) = 1.066e-2 = (Ca+2) + (CaCO3)
2a. 9.5/10.7 ~ 0.95
2b. 1.063/1.066 ~ 1.0
3a. 3.509e-019 / 3.711e-008 ~ 1e-11
3b. No Fe+3 ion.
4a. log activity CO3-2 = -5.091; log gamma CO3-2 = -0.68
4b. Log activity CO3-2 = -5.099; log gamma CO3-2 = -1.09
5a. SI(calcite) = 0.76
5b. SI(calcite) = 0.70
Input file: H:\ntc\07\Solutions.working\is2.pqi
Output file: H:\ntc\07\Solutions.working\is2.pqo
Database file: C:\Program Files\USGS\Phreeqc Interactive 2.13.2\phreeqc.dat
------------------
Reading data base.
------------------
SOLUTION_MASTER_SPECIES
SOLUTION_SPECIES
PHASES
EXCHANGE_MASTER_SPECIES
EXCHANGE_SPECIES
SURFACE_MASTER_SPECIES
SURFACE_SPECIES
RATES
END
------------------------------------
Reading input data for simulation 1.
------------------------------------
DATABASE C:\Program Files\USGS\Phreeqc Interactive 2.13.2\phreeqc.dat
SOLUTION 1
temp 25
pH 8.22
pe 8.45
redox pe
units ppm
density 1
Ca 412.3
Mg 1291.8
Na 10768
K 399.1
Fe 0.002
Alkalinity 141.682 as HCO3
Cl 19353
S(6) 2712
water 1 # kgg
-------------------------------------------
Beginning of initial solution calculations.
-------------------------------------------
Initial solution 1.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Alkalinity 2.406e-003 2.406e-003
Ca 1.066e-002 1.066e-002
Cl 5.657e-001 5.657e-001
Fe 3.711e-008 3.711e-008
K 1.058e-002 1.058e-002
Mg 5.507e-002 5.507e-002
Na 4.854e-001 4.854e-001
S(6) 2.926e-002 2.926e-002
----------------------------Description of solution----------------------------
pH = 8.220
pe = 8.450
Activity of water = 0.981
Ionic strength = 6.748e-001
Mass of water (kg) = 1.000e+000
Total carbon (mol/kg) = 2.182e-003
Total CO2 (mol/kg) = 2.182e-003
Temperature (deg C) = 25.000
Electrical balance (eq) = 7.967e-004
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 0.07
Iterations = 7
Total H = 1.110144e+002
Total O = 5.562980e+001
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 2.674e-006 1.629e-006 -5.573 -5.788 -0.215
H+ 7.981e-009 6.026e-009 -8.098 -8.220 -0.122
H2O 5.551e+001 9.806e-001 1.744 -0.009 0.000
C(4) 2.182e-003
HCO3- 1.516e-003 1.024e-003 -2.819 -2.990 -0.170
MgHCO3+ 2.198e-004 1.642e-004 -3.658 -3.785 -0.127
NaHCO3 1.669e-004 1.950e-004 -3.777 -3.710 0.067
MgCO3 8.924e-005 1.042e-004 -4.049 -3.982 0.067
NaCO3- 6.726e-005 5.026e-005 -4.172 -4.299 -0.127
CaHCO3+ 4.603e-005 3.110e-005 -4.337 -4.507 -0.170
CO3-2 3.826e-005 7.969e-006 -4.417 -5.099 -0.681
CaCO3 2.728e-005 3.187e-005 -4.564 -4.497 0.067
CO2 1.211e-005 1.415e-005 -4.917 -4.849 0.067
FeCO3 1.700e-016 1.985e-016 -15.770 -15.702 0.067
FeHCO3+ 1.423e-016 1.063e-016 -15.847 -15.973 -0.127
Ca 1.066e-002
Ca+2 9.504e-003 2.380e-003 -2.022 -2.623 -0.601
CaSO4 1.083e-003 1.265e-003 -2.965 -2.898 0.067
CaHCO3+ 4.603e-005 3.110e-005 -4.337 -4.507 -0.170
CaCO3 2.728e-005 3.187e-005 -4.564 -4.497 0.067
CaOH+ 8.604e-008 6.429e-008 -7.065 -7.192 -0.127
CaHSO4+ 5.979e-011 4.467e-011 -10.223 -10.350 -0.127
Cl 5.657e-001
Cl- 5.657e-001 3.528e-001 -0.247 -0.452 -0.205
FeCl+ 6.769e-016 5.058e-016 -15.169 -15.296 -0.127
FeCl+2 9.556e-019 2.978e-019 -18.020 -18.526 -0.506
FeCl2+ 6.281e-019 4.693e-019 -18.202 -18.329 -0.127
FeCl3 1.417e-020 1.656e-020 -19.849 -19.781 0.067
Fe(2) 6.007e-015
Fe+2 4.525e-015 1.039e-015 -14.344 -14.984 -0.639
FeCl+ 6.769e-016 5.058e-016 -15.169 -15.296 -0.127
FeSO4 4.213e-016 4.921e-016 -15.375 -15.308 0.067
FeCO3 1.700e-016 1.985e-016 -15.770 -15.702 0.067
FeHCO3+ 1.423e-016 1.063e-016 -15.847 -15.973 -0.127
FeOH+ 7.153e-017 5.345e-017 -16.145 -16.272 -0.127
FeHSO4+ 2.609e-023 1.949e-023 -22.584 -22.710 -0.127
Fe(3) 3.711e-008
Fe(OH)3 2.840e-008 3.318e-008 -7.547 -7.479 0.067
Fe(OH)4- 6.591e-009 4.924e-009 -8.181 -8.308 -0.127
Fe(OH)2+ 2.118e-009 1.583e-009 -8.674 -8.801 -0.127
FeOH+2 9.425e-014 2.937e-014 -13.026 -13.532 -0.506
FeSO4+ 1.093e-018 8.167e-019 -17.961 -18.088 -0.127
FeCl+2 9.556e-019 2.978e-019 -18.020 -18.526 -0.506
FeCl2+ 6.281e-019 4.693e-019 -18.202 -18.329 -0.127
Fe+3 3.509e-019 2.795e-020 -18.455 -19.554 -1.099
Fe(SO4)2- 6.371e-020 4.761e-020 -19.196 -19.322 -0.127
FeCl3 1.417e-020 1.656e-020 -19.849 -19.781 0.067
Fe2(OH)2+4 2.462e-024 2.322e-026 -23.609 -25.634 -2.025
FeHSO4+2 4.228e-026 1.318e-026 -25.374 -25.880 -0.506
Fe3(OH)4+5 1.122e-029 7.678e-033 -28.950 -32.115 -3.165
H(0) 5.540e-037
H2 2.770e-037 3.236e-037 -36.557 -36.490 0.067
K 1.058e-002
K+ 1.041e-002 6.495e-003 -1.982 -2.187 -0.205
KSO4- 1.627e-004 1.216e-004 -3.789 -3.915 -0.127
KOH 3.137e-009 3.665e-009 -8.503 -8.436 0.067
Mg 5.507e-002
Mg+2 4.742e-002 1.371e-002 -1.324 -1.863 -0.539
MgSO4 7.330e-003 8.562e-003 -2.135 -2.067 0.067
MgHCO3+ 2.198e-004 1.642e-004 -3.658 -3.785 -0.127
MgCO3 8.924e-005 1.042e-004 -4.049 -3.982 0.067
MgOH+ 1.084e-005 8.100e-006 -4.965 -5.092 -0.127
Na 4.854e-001
Na+ 4.791e-001 3.387e-001 -0.320 -0.470 -0.151
NaSO4- 6.053e-003 4.523e-003 -2.218 -2.345 -0.127
NaHCO3 1.669e-004 1.950e-004 -3.777 -3.710 0.067
NaCO3- 6.726e-005 5.026e-005 -4.172 -4.299 -0.127
NaOH 3.117e-007 3.641e-007 -6.506 -6.439 0.067
O(0) 6.554e-020
O2 3.277e-020 3.828e-020 -19.485 -19.417 0.067
S(6) 2.926e-002
SO4-2 1.463e-002 2.664e-003 -1.835 -2.574 -0.740
MgSO4 7.330e-003 8.562e-003 -2.135 -2.067 0.067
NaSO4- 6.053e-003 4.523e-003 -2.218 -2.345 -0.127
CaSO4 1.083e-003 1.265e-003 -2.965 -2.898 0.067
KSO4- 1.627e-004 1.216e-004 -3.789 -3.915 -0.127
HSO4- 2.089e-009 1.561e-009 -8.680 -8.807 -0.127
CaHSO4+ 5.979e-011 4.467e-011 -10.223 -10.350 -0.127
FeSO4 4.213e-016 4.921e-016 -15.375 -15.308 0.067
FeSO4+ 1.093e-018 8.167e-019 -17.961 -18.088 -0.127
Fe(SO4)2- 6.371e-020 4.761e-020 -19.196 -19.322 -0.127
FeHSO4+ 2.609e-023 1.949e-023 -22.584 -22.710 -0.127
FeHSO4+2 4.228e-026 1.318e-026 -25.374 -25.880 -0.506
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Anhydrite -0.84 -5.20 -4.36 CaSO4
Aragonite 0.61 -7.72 -8.34 CaCO3
Calcite 0.76 -7.72 -8.48 CaCO3
CO2(g) -3.38 -4.85 -1.47 CO2
Dolomite 2.41 -14.68 -17.09 CaMg(CO3)2
Fe(OH)3(a) 0.19 5.08 4.89 Fe(OH)3
Goethite 6.09 5.09 -1.00 FeOOH
Gypsum -0.63 -5.21 -4.58 CaSO4:2H2O
H2(g) -33.34 -36.49 -3.15 H2
H2O(g) -1.52 -0.01 1.51 H2O
Halite -2.50 -0.92 1.58 NaCl
Hematite 14.20 10.19 -4.01 Fe2O3
Jarosite-K -7.52 -16.73 -9.21 KFe3(SO4)2(OH)6
Melanterite -15.41 -17.62 -2.21 FeSO4:7H2O
O2(g) -16.52 -19.42 -2.89 O2
Siderite -9.19 -20.08 -10.89 FeCO3
------------------
End of simulation.
------------------
------------------------------------
Reading input data for simulation 2.
------------------------------------
-----------
End of run.
-----------

## Slide 30: Initial Solution 2a. Questions
Write the mass-action equation for the reaction: CO2 + H2O = HCO3- + H+.
Write the mass-action equation for question 1 in log form.
Calculate the equilibrium constant by using the log activities from the speciation results.
At what pH will activity [CO2] equal activity [HCO3-]?
<number>
Notes: <number>
IS.2a. Questions
() indicates molality
[] indicates activity
1. K = [HCO3-][H+]/([CO2][H2O])
2. Log K = log([HCO3-]) + log([H+]) - log([CO2]) + log([H2O])
3. Log K = -2.99 + (-8.22) – (-4.85) – (–.009) = – 6.351
4. pH 6.35

## Slide 31: Initial Solution 2. Answers
() indicates molality
1a. Ca(total)= 1.066e-2 = (Ca+2) + (CaSO4) + (CaHCO3+) + (CaCO3) + (CaOH+) + (CaHSO4+)
1b. Ca(total) = 1.066e-2 = (Ca+2) + (CaCO3)
2a. 9.5/10.7 ~ 0.95
2b. 1.063/1.066 ~ 1.0
3a. 3.509e-019 / 3.711e-008 ~ 1e-11
3b. No Fe+3 ion.
4a. log activity CO3-2 = -5.099; log gamma CO3-2 = -0.68
4b. log activity CO3-2 = -5.091; log gamma CO3-2 = -1.09
5a. SI(calcite) = 0.76
5b. SI(calcite) = 0.70
<number>

## Slide 32: Initial Solution 2a. Answers
K = [HCO3-][H+]/([CO2][H2O])
Log K = log([HCO3-]) + log([H+]) - log([CO2]) + log([H2O])
Log K = -2.99 + (-8.22) - (- 4.849) - (-0.009) = -6.352
~pH 6.35
<number>

## Slide 33: More on Solution Definition
pH, Carbon, Alkalinity
<number>
Notes: <number>

## Slide 34: What is pH?
Questions
1. How does the pH change when CO2 degasses during an alkalinity titration?
2. How does pH change when plankton respire CO2?
3. How does pH change when calcite dissolves?
pH = 6.3 + log[(HCO3-)/(CO2)]
pH = 10.3 + log[(CO3-2)/(HCO3-)]
<number>
Notes: <number>
IS.3. Questions
1. CO2 decreases, pH increases.
2. CO2 increases, pH decreases.
3. CaCO3 + CO2 + H2O = Ca+2 + 2HCO3-; CO2 decreases, HCO3- increases, pH increases.

## Slide 35: Alkalinity
Effectively, the alkalinity is the number of equivalents of H+ needed to convert all of the inorganic carbon to CO2 (aq or g)
HCO3- + H+ = CO2 + H2O
Alkalinity is independent of PCO2
Total Inorganic Carbon
Number of moles of carbon of valence 4
<number>

## Slide 36: SOLUTION_SPREAD
SELECTED_OUTPUT
<number>
Notes: <number>

## Slide 37: SOLUTION_SPREAD
<number>
Notes: <number>

## Slide 38: SELECTED_OUTPUT
1.Reset all to false
File name
2. Set pH to true
<number>
Notes: <number>

## Slide 39: SELECTED_OUTPUT--Molalities
Select species
<number>
Notes: <number>

## Slide 40: Initial Solution 4a. Exercises
pH | C
4 | 1
5 | 1
6 | 1
7 | 1
8 | 1
9 | 1
10 | 1
11 | 1
12 | 1
Concentration in mmol/kgw
1. Make speciation calculations for these 9 solution compositions with SOLUTION _SPREAD.
2. Make a table of pH, (CO2), (HCO3-), (CO3-2) with SELECTED_OUTPUT. Plot pH vs. concentrations in Excel
<number>
Notes: <number>
# IS 4a Exercise
SOLUTION_SPREAD
pH C
4 1
5 1
6 1
7 1
8 1
9 1
10 1
11 1
12 1
SELECTED_OUTPUT
-file is4a.sel
-reset false
-ph true
-molalities CO2 HCO3- CO3-2
END

## Slide 41: Initial Solution 4b. Exercises
pH | Alkalinity
6 | 2
7 | 2
8 | 2
9 | 2
10 | 2
11 | 2
Concentration in meq/kgw
1. Make speciation calculations for these 6 solution compositions with SOLUTION _SPREAD.
2. Use SELECTED_OUTPUT to make a table of pH, (CO2), (HCO3-), (CO3-2), total C (use TOTALS tab). Plot pH vs. concentrations in Excel.
<number>
Notes: <number>
# IS 4b. Exercise
SOLUTION_SPREAD
pH Alkalinity
6 2
7 2
8 2
9 2
10 2
11 2
SELECTED_OUTPUT
-file is4b.sel
-reset false
-ph true
-totals C
-molalities CO2 HCO3- CO3-2
END

## Slide 42: Initial Solution 4. Questions
1. Write a definition of total carbon(4) (sometimes called total CO2 or TDIC) in terms of (CO2), (HCO3-), (CO3-2).
2. Write a definition of alkalinity in terms of (CO2), (HCO3-), (CO3-2).
3. Include (OH-) in your definition.
4. Include (H+) in your definition.
<number>
Notes: <number>
IS 4. Questions
1. Total CO2 = (CO2) + (HCO3-) + (CO3-2)
2. Alkalinity = (HCO3-) + 2(CO3-2)
3. Alkalinity = (HCO3-) + 2(CO3-2) + (OH-)
4. Alkalinity = (HCO3-) + 2(CO3-2) + (OH-) – (H+)

## Slide 43: Fixed Total Carbon
<number>

## Slide 44: Fixed Alkalinity
<number>

## Slide 45: Initial Solution 4. Answers
Total CO2 = (CO2) + (HCO3-) + (CO3-2)
Alkalinity = (HCO3-) + 2(CO3-2)
Alkalinity = (HCO3-) + 2(CO3-2) + (OH-)
Alkalinity = (HCO3-) + 2(CO3-2) + (OH-) – (H+)
<number>

## Slide 46: More on Solution Definition
Redox, pe
<number>
Notes: <number>

## Slide 47: What is pe?
Fe+2 = Fe+3 + e-
pe = log( [Fe+3]/[Fe+2] ) + 13
HS- + 4H2O = SO4-2 + 9H+ + 8e-
pe = log( [SO4-2]/[HS-] ) – 9/8pH + 4.21
N2 + 6H2O = 2NO3- + 12H+ + 10e-
pe = 0.1log( [NO3-]2/[N2] ) –1.2pH + 20.7
pe = 16.9Eh, Eh in volts (platinum electrode measurement)
<number>
Notes: <number>

## Slide 48: Initial Solution 7. Question
1. Write an equation for pe from the equation for oxidation of NH4+ to NO3-, log K for reaction is –119.1.
Hint: Chemical reaction has NH4+ and H2O on the left-hand-side and NO3-, H+, and e- on the right-hand-side.
<number>
Notes: <number>
IS.7. Questions
1. NH4+ + 3H2O = NO3- + 10H+ + 8e-
Log K = -119.1 = log[NO3-] – 10pH – 8pe – log[NH4+] - 3log[H2O]
8pe = log[NO3-] – log[NH4+] + 119.1 – 10pH – 3log[H2O]
pe = 1/8log( [NO3-] / [NH4+] ) – 10/8pH + 14.9 – 3/8log[H2O]

## Slide 49: Initial Solution 7. Answer
NH4+ + 3H2O = NO3- + 10H+ + 8e-
Log K = -119.1 = log[NO3-] – 10pH – 8pe – log[NH4+] - 3log[H2O]
8pe = log[NO3-] – log[NH4+] + 119.1 – 10pH – 3log[H2O]
pe = 1/8log( [NO3-] / [NH4+] ) – 10/8pH + 14.9 – 3/8log[H2O]
<number>

## Slide 50: More on pe
Aqueous electrons do not exist
Redox reactions are frequently not in equilibrium
Multiple pes from multiple redox couples
However, we do not expect to see major inconsistencies—e.g. both D.O. and HS-—in a single environment
<number>
Notes: <number>

## Slide 51: Redox and pe in SOLUTION Data Blocks
When do you need pe for SOLUTION?
  To distribute total concentration of a redox element among redox states [e.g. Fe to Fe(2) and Fe(3)]
  A few saturation indices with e- in dissociation reactions
    Pyrite
    Native sulfur
    Manganese oxides
Can use a redox couple Fe(2)/Fe(3) in place of pe
Rarely, pe = 16.9Eh. (25 C and Eh in Volts).
pe options can only be applied to speciation calculations; thermodynamic pe is used for all other calculations
<number>
Notes: <number>

## Slide 52: Redox Elements
Element | Redox state | Species
Carbon | C(4) | CO2
 | C(-4) | CH4
Sulfur | S(6) | SO4-2
 | S(-2) | HS-
Nitrogen | N(5) | NO3-
 | N(3) | NO2-
 | N(0) | N2
 | N(-3) | NH4+
Oxygen | O(0) | O2
 | O(-2) | H2O
Hydrogen | H(1) | H2O
 | H(0) | H2
Element | Redox state | Species
Iron | Fe(3) | Fe+3
 | Fe(2) | Fe+2
Manganese | Mn(2) | Mn+2
Arsenic | As(5) | AsO4-3
 | As(3) | AsO3-3
Uranium | U(6) | UO2+2
 | U(4) | U+4
Chromium | Cr(6) | CrO4-2
 | Cr(3) | Cr+3
Selenium | Se(6) | SeO4-2
 | Se(4) | SeO3-2
 | Se(-2) | HSe-
<number>
Notes: <number>

## Slide 53: Using Redox Couples
Double click to get list of redox couples
Must have analyses for chosen redox couple
<number>
Notes: <number>

## Slide 54: Seawater Initial Solution
Fe total was entered. How were Fe(3) and Fe(2) concentrations calculated?
For initial solutions
For “reactions”
<number>

## Slide 55: Iron Speciation with PhreePlot
<number>
Notes: <number>

## Slide 56: Initial Solution 8. Exercise
Constituent | 1 | 2 | 3 | 4
pH | 7.0 | 7.0 | 7.0 | 7.0
pe | 0.0 | 0.0 | 0.0 | 0.0
Redox | pe | pe | pe | Fe(2)/Fe(3)
Fe, mmol/kgw | 1.0 |  |  | 
Fe(2) , mmol/kgw |  | 1.0 |  | 1.0
Fe(3) , mmol/kgw |  |  | 1.0 | 1.0
Solution number
Define SOLUTIONs and run calculations.
<number>
Notes: <number>
# IS.8 Exercise
SOLUTION 1
pH 7
pe 0
redox pe
Fe 1
SOLUTION 2
pH 7
pe 0
redox pe
Fe(2) 1
SOLUTION 3
pH 7
pe 0
redox pe
Fe(3) 1
SOLUTION 4
pH 7
pe 0
redox Fe(2)/Fe(3)
Fe(2) 1
Fe(3) 1

## Slide 57: Initial Solution 8. Exercise
Element | 1 | 2 | 3 | 4
Total iron |  |  |  | 
Total ferrous iron |  |  |  | 
Total ferric iron |  |  |  | 
pe from Fe(3)/Fe(2) | -- | -- | -- | 
Saturation Index Fe(OH)3(a) |  |  |  | 
Saturation Index Goethite |  |  |  | 
Solution number
Fill in the table.
<number>
Notes: <number>
1 2 3 4
Total iron 1.0 1.0 1.0 2.0
Total ferrous iron 1.0 1.0 0 1.0
Total ferric iron 3e-8 0 1.0 1.0
Fe(3)/Fe(2) pe -- -- -- 4.4
SI Fe(OH)3(a) 0 - 4.4 4.4
SI Goethite 5.9 - 10.3 10.3
Input file: C:\NTC\07\Solutions.working\is8.pqi
Output file: C:\NTC\07\Solutions.working\is8.pqo
Database file: C:\Program Files\USGS\Phreeqc Interactive 2.13.2\phreeqc.dat
------------------
Reading data base.
------------------
SOLUTION_MASTER_SPECIES
SOLUTION_SPECIES
PHASES
EXCHANGE_MASTER_SPECIES
EXCHANGE_SPECIES
SURFACE_MASTER_SPECIES
SURFACE_SPECIES
RATES
END
------------------------------------
Reading input data for simulation 1.
------------------------------------
DATABASE C:\Program Files\USGS\Phreeqc Interactive 2.13.2\phreeqc.dat
SOLUTION 1
pH 7
pe 0
redox pe
Fe 1
SOLUTION 2
pH 7
pe 0
redox pe
Fe(2) 1
SOLUTION 3
pH 7
pe 0
redox pe
Fe(3) 1
SOLUTION 4
pH 7
pe 0
redox Fe(2)/Fe(3)
Fe(2) 1
Fe(3) 1
-------------------------------------------
Beginning of initial solution calculations.
-------------------------------------------
Initial solution 1.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Fe 1.000e-003 1.000e-003
----------------------------Description of solution----------------------------
pH = 7.000
pe = 0.000
Activity of water = 1.000
Ionic strength = 1.996e-003
Mass of water (kg) = 1.000e+000
Total alkalinity (eq/kg) = 2.755e-006
Total carbon (mol/kg) = 0.000e+000
Total CO2 (mol/kg) = 0.000e+000
Temperature (deg C) = 25.000
Electrical balance (eq) = 1.997e-003
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 99.99
Iterations = 4
Total H = 1.110124e+002
Total O = 5.550622e+001
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 1.052e-007 1.001e-007 -6.978 -7.000 -0.022
H+ 1.047e-007 1.000e-007 -6.980 -7.000 -0.020
H2O 5.551e+001 1.000e+000 1.744 -0.000 0.000
Fe(2) 1.000e-003
Fe+2 9.972e-004 8.225e-004 -3.001 -3.085 -0.084
FeOH+ 2.733e-006 2.601e-006 -5.563 -5.585 -0.021
Fe(3) 3.948e-008
Fe(OH)3 2.162e-008 2.163e-008 -7.665 -7.665 0.000
Fe(OH)2+ 1.764e-008 1.679e-008 -7.753 -7.775 -0.021
Fe(OH)4- 2.073e-010 1.973e-010 -9.683 -9.705 -0.021
FeOH+2 6.181e-012 5.071e-012 -11.209 -11.295 -0.086
Fe+3 1.191e-016 7.855e-017 -15.924 -16.105 -0.181
Fe2(OH)2+4 1.527e-021 6.923e-022 -20.816 -21.160 -0.344
Fe3(OH)4+5 8.362e-027 2.429e-027 -26.078 -26.615 -0.537
H(0) 1.415e-017
H2 7.076e-018 7.079e-018 -17.150 -17.150 0.000
O(0) 0.000e+000
O2 0.000e+000 0.000e+000 -58.080 -58.080 0.000
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Fe(OH)3(a) 0.00 4.90 4.89 Fe(OH)3
Goethite 5.90 4.90 -1.00 FeOOH
H2(g) -14.00 -17.15 -3.15 H2
H2O(g) -1.51 -0.00 1.51 H2O
Hematite 13.80 9.79 -4.01 Fe2O3
O2(g) -55.19 -58.08 -2.89 O2
Initial solution 2.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Fe(2) 1.000e-003 1.000e-003
----------------------------Description of solution----------------------------
pH = 7.000
pe = 0.000
Activity of water = 1.000
Ionic strength = 1.996e-003
Mass of water (kg) = 1.000e+000
Total alkalinity (eq/kg) = 2.733e-006
Total carbon (mol/kg) = 0.000e+000
Total CO2 (mol/kg) = 0.000e+000
Temperature (deg C) = 25.000
Electrical balance (eq) = 1.997e-003
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 99.99
Iterations = 4
Total H = 1.110124e+002
Total O = 5.550622e+001
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 1.052e-007 1.001e-007 -6.978 -7.000 -0.022
H+ 1.047e-007 1.000e-007 -6.980 -7.000 -0.020
H2O 5.551e+001 1.000e+000 1.744 -0.000 0.000
Fe(2) 1.000e-003
Fe+2 9.973e-004 8.225e-004 -3.001 -3.085 -0.084
FeOH+ 2.733e-006 2.601e-006 -5.563 -5.585 -0.021
H(0) 1.415e-017
H2 7.076e-018 7.079e-018 -17.150 -17.150 0.000
O(0) 0.000e+000
O2 0.000e+000 0.000e+000 -58.080 -58.080 0.000
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
H2(g) -14.00 -17.15 -3.15 H2
H2O(g) -1.51 -0.00 1.51 H2O
O2(g) -55.19 -58.08 -2.89 O2
Initial solution 3.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Fe(3) 1.000e-003 1.000e-003
----------------------------Description of solution----------------------------
pH = 7.000
pe = 0.000
Activity of water = 1.000
Ionic strength = 2.224e-004
Mass of water (kg) = 1.000e+000
Total alkalinity (eq/kg) = 5.660e-004
Total carbon (mol/kg) = 0.000e+000
Total CO2 (mol/kg) = 0.000e+000
Temperature (deg C) = 25.000
Electrical balance (eq) = 4.340e-004
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 97.63
Iterations = 4
Total H = 1.110150e+002
Total O = 5.550878e+001
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 1.018e-007 1.001e-007 -6.992 -7.000 -0.007
H+ 1.017e-007 1.000e-007 -6.993 -7.000 -0.007
H2O 5.551e+001 1.000e+000 1.744 -0.000 0.000
Fe(3) 1.000e-003
Fe(OH)3 5.558e-004 5.558e-004 -3.255 -3.255 0.000
Fe(OH)2+ 4.389e-004 4.315e-004 -3.358 -3.365 -0.007
Fe(OH)4- 5.157e-006 5.069e-006 -5.288 -5.295 -0.007
FeOH+2 1.396e-007 1.303e-007 -6.855 -6.885 -0.030
Fe+3 2.347e-012 2.018e-012 -11.630 -11.695 -0.065
Fe2(OH)2+4 6.013e-013 4.570e-013 -12.221 -12.340 -0.119
Fe3(OH)4+5 6.325e-014 4.119e-014 -13.199 -13.385 -0.186
H(0) 1.416e-017
H2 7.079e-018 7.079e-018 -17.150 -17.150 0.000
O(0) 0.000e+000
O2 0.000e+000 0.000e+000 -58.080 -58.080 0.000
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Fe(OH)3(a) 4.41 9.30 4.89 Fe(OH)3
Goethite 10.30 9.30 -1.00 FeOOH
H2(g) -14.00 -17.15 -3.15 H2
H2O(g) -1.51 -0.00 1.51 H2O
Hematite 22.62 18.61 -4.01 Fe2O3
O2(g) -55.19 -58.08 -2.89 O2
Initial solution 4.
-----------------------------Solution composition------------------------------
Elements Molality Moles
Fe(2) 1.000e-003 1.000e-003
Fe(3) 1.000e-003 1.000e-003
----------------------------Description of solution----------------------------
pH = 7.000
pe = 0.000
Activity of water = 1.000
Ionic strength = 2.223e-003
Mass of water (kg) = 1.000e+000
Total alkalinity (eq/kg) = 5.601e-004
Total carbon (mol/kg) = 0.000e+000
Total CO2 (mol/kg) = 0.000e+000
Temperature (deg C) = 25.000
Electrical balance (eq) = 2.440e-003
Percent error, 100*(Cat-|An|)/(Cat+|An|) = 99.56
Iterations = 4
Total H = 1.110150e+002
Total O = 5.550878e+001
---------------------------------Redox couples---------------------------------
Redox couple pe Eh (volts)
Fe(2)/Fe(3) 4.4073 0.2607
----------------------------Distribution of species----------------------------
Log Log Log
Species Molality Activity Molality Activity Gamma
OH- 1.055e-007 1.001e-007 -6.977 -7.000 -0.023
H+ 1.050e-007 1.000e-007 -6.979 -7.000 -0.021
H2O 5.551e+001 1.000e+000 1.744 -0.000 0.000
Fe(2) 1.000e-003
Fe+2 9.973e-004 8.146e-004 -3.001 -3.089 -0.088
FeOH+ 2.713e-006 2.576e-006 -5.566 -5.589 -0.023
Fe(3) 1.000e-003
Fe(OH)3 5.470e-004 5.473e-004 -3.262 -3.262 0.000
Fe(OH)2+ 4.476e-004 4.249e-004 -3.349 -3.372 -0.023
Fe(OH)4- 5.258e-006 4.991e-006 -5.279 -5.302 -0.023
FeOH+2 1.580e-007 1.283e-007 -6.801 -6.892 -0.090
Fe+3 3.076e-012 1.987e-012 -11.512 -11.702 -0.190
Fe2(OH)2+4 1.019e-012 4.431e-013 -11.992 -12.353 -0.361
Fe3(OH)4+5 1.444e-013 3.934e-014 -12.840 -13.405 -0.565
H(0) 2.168e-026
H2 1.084e-026 1.085e-026 -25.965 -25.965 0.000
O(0) 0.000e+000
O2 0.000e+000 0.000e+000 -40.451 -40.451 0.000
------------------------------Saturation indices-------------------------------
Phase SI log IAP log KT
Fe(OH)3(a) 4.41 9.30 4.89 Fe(OH)3
Goethite 10.30 9.30 -1.00 FeOOH
H2(g) -22.81 -25.96 -3.15 H2
H2O(g) -1.51 -0.00 1.51 H2O
Hematite 22.60 18.60 -4.01 Fe2O3
O2(g) -37.56 -40.45 -2.89 O2
------------------
End of simulation.
------------------
------------------------------------
Reading input data for simulation 2.
------------------------------------
-----------
End of run.
-----------

## Slide 58: Initial Solution 8. Questions
1. For each solution
  Explain the distribution of Fe between Fe(2) and Fe(3).
  This equation is used for goethite SI: FeOOH + 3H+ = Fe+3 + 2H2O Explain why the goethite saturation index is present or absent.
2. What pe is calculated for solution 4?
3. In solution 4, given the following equation, why is the pe not 13?
pe = log( [Fe+3]/[Fe+2] ) + 13
4. For pH > 5, it is a good assumption that the measured iron concentration is nearly all Fe(2) (ferrous). How can you ensure that the speciation calculation is consistent with this assumption?
<number>
Notes: <number>
IS.8. Questions
Questions 1:
Solution 1:
a. Fe distributed by using pe 0, Fe(2) and Fe(3) defined.
b. Fe(3) is defined, goethite SI can be calculated.
Solution 2:
a. Fe(2) is defined to be 1 mmol/kgw.
Fe(3) is undefined.
b. Fe(3) is not defined, goethite SI can not be calculated.
Solution 3:
a. Fe(2) is undefined.
Fe(3) is defined to be 1 mmol/kgw.
b. Fe(3) is defined, goethite SI can be calculated.
Solution 4:
a. Fe(2) and Fe(3) defined.
b. Fe(3) is defined, goethite SI can be calculated.
Question 2:
pe from Fe(2)/Fe(3) couple is 4.4.
Question 3:
The equation is for the activity of Fe+3 and Fe+2 ions. In solution, we defined the sum of the molalities of the Fe(3) and Fe(2) species. Fe(2) is predominantly (Fe+2) ion, but Fe(OH)3 and Fe(OH)2+ are the predominant Fe(3) species. (Fe+3) is 8 orders of magnitude less than the predominant species.
Question 4:
Define iron as Fe(2) or adjust pe sufficiently low to produce mostly Fe(2). Note: goethite SI will not be calculated in the first case and will be completely dependent on your choice of pe for the second.

## Slide 59: Initial Solution 8. Answers
Element | 1 | 2 | 3 | 4
Total iron | 1.0 | 1.0 | 1.0 | 2.0
Total ferrous iron | 1.0 | 1.0 | 0 | 1.0
Total ferric iron | 3e-8 | 0 | 1.0 | 1.0
pe from Fe(3)/Fe(2) | -- | -- | -- | 4.4
Saturation Index Fe(OH)3(a) | 0 | ? | 4.4 | 4.4
Saturation Index Goethite | 5.9 | ? | 10.3 | 10.3
Solution number
Fill in the table.
<number>
Notes: <number>

## Slide 60: Initial Solution 8. Answers
1. Solution 1:
a. Fe distributed by using pe 0, Fe(2) and Fe(3) defined.
b. Fe(3) is defined, goethite SI can be calculated.
Solution 2:
a. Fe(2) is defined to be 1 mmol/kgw.
Fe(3) is undefined.
b. Fe(3) is not defined, goethite SI can not be calculated.
Solution 3:
a. Fe(2) is undefined.
Fe(3) is defined to be 1 mmol/kgw.
b. Fe(3) is defined, goethite SI can be calculated.
Solution 4:
a. Fe(2) and Fe(3) defined.
b. Fe(3) is defined, goethite SI can be calculated.
2. pe from Fe(2)/Fe(3) couple is 4.4.
3. The equation is for the activity of Fe+3 and Fe+2 ions. In solution, we defined the sum of the molalities of the Fe(3) and Fe(2) species. Fe(2) is predominantly (Fe+2) ion, but Fe(OH)3 and Fe(OH)2+ are the predominant Fe(3) species. (Fe+3) is 8 orders of magnitude less than the predominant species.
4. Define iron as Fe(2) or adjust pe sufficiently low to produce mostly Fe(2). Note: goethite SI will not be calculated in the first case and will be completely dependent on your choice of pe for the second.
<number>

## Slide 61: Final thoughts on pe
pe is used to distribute total redox element concentration among redox states, but often not needed.
Possible measurements of total concentrations of redox elements:
  Fe, always Fe(2) except at low pH
  Mn, always Mn(2)
  As, consider other redox elements
  Se, consider other redox elements
  U, probably U(6)
  V, probably V(5)
<number>

## Slide 62: Final thoughts on pe
Use couples where available:
O(0)/O(-2)
N(5)/N(-3)
S(6)/S(-2)
Fe(3)/Fe(2)
As(5)/As(3)
<number>

## Slide 63: Berner’s Redox Environments
Oxic
Suboxic
Sulfidic
Methanic
Thorstenson (1984)
<number>

## Slide 64
<number>

## Slide 65
Parkhurst and others (1996)
<number>

## Slide 66: PHREEQC Programs
Current PHREEQC Version 2
  Batch
  GUI PhreeqcI
  GUI Phreeqc For Windows (Vincent Post)
Current PHAST Version 2
  Serial
  Parallel chemistry
<number>

## Slide 67: Future PHREEQC Programs
PHREEQC Version 3
  Batch with Charting (done)
  GUI PhreeqcI with Charting
  IPhreeqc: scriptable (done)
PHAST
  Serial (done)
  Parallel transport and chemistry (done)
  TVD
  GUI PHAST for Windows
WEBMOD-Watershed reactive transport
<number>

## Slide 68: More on Solution Definition
Charge Balance and Adjustment to Phase Equilibrium
<number>
Notes: <number>

## Slide 69: Charge Balance Options
For most analyses, just leave it
Adjust the major anion or cation
Adjust pH
<number>
Notes: <number>

## Slide 70: SOLUTION Charge Balance
Select pH or major ion
No way to specify cation or anion
<number>
Notes: <number>

## Slide 71: Initial Solution 10. Exercises
Define a solution made by adding 1 mmol of NaHCO3 and 1 mmol Na2CO3 to a kilogram of water. What is the pH of the solution?
Hint: The solution definition contains Na and C(4).
2. Define a solution made by adding 1 mmol of NaHCO3 and 1 mmol Na2CO3 to a kilogram of water that was then titrated to pH 7 with pure HCl. How much chloride was added?
Hint: The solution definition contains Na, C, and Cl.
<number>
Notes: <number>
IS.10. Exercises
# IS.10 Exercise
SOLUTION 1
pH 7 charge
Na 3
C 2
END
SOLUTION 2
pH 7
Na 3
C 2
Cl 1 charge
END
Answers:
pH = 10.1
Cl = 1.35 mmol

## Slide 72: Initial Solution 10. Answers
pH = 10.1
Cl = 1.35 mmol
<number>

## Slide 73: Adjustments to Phase Equilibrium
For most analyses, don’t do it
The following are reasonable
  Adjust concentrations to equilibrium with atmosphere (O2, CO2)
  Adjust pH to calcite equilibrium
  Estimate aluminum concentration by equilibrium with gibbsite or kaolinite
<number>
Notes: <number>

## Slide 74: Adjusting to Phase Equilibrium with SOLUTION
Select Phase
Add saturation index for mineral, log partial pressure for gas
<number>
Notes: <number>

## Slide 75: Adjusting to Phase Equilibrium with SOLUTION_SPREAD
Select phase
Define SI or log partial pressure
<number>
Notes: <number>

## Slide 76: UNITS in SOLUTION_SPREAD
Don’t forget to set the units!
<number>
Notes: <number>

## Slide 77: Initial Solution 11. Exercise
1. Calculate the carbon concentration that would be in equilibrium with the atmosphere (log PCO2 = -3.5).
Constituent | Value | Constituent | Value
pH | 4.5 | Cl | 0.236
Ca | 0.384 | S(6) | 1.3
Mg | 0.043 | N(5) | 0.237
Na | 0.141 | N(-3) | 0.208
K | 0.036 | P | 0.0003
C(4) | ? |  | 
Rainwater, Concentration in mg/L
<number>
Notes: <number>
# IS.11. Exercise
SOLUTION 1
temp 25
pH 4.5
pe 4
redox pe
units mg/l
density 1
Ca 0.384
Mg 0.043
Na 0.141
K 0.036
C(4) 1 CO2(g) -3.5
Cl 0.236
S(6) 1.3
N(5) 0.237
N(-3) 0.208
P 0.0003
-water 1 # kg
END
Answer:
1. 1.1e-5 mol/kgwater

## Slide 78: Initial Solution 11. Answer
Calculate the carbon concentration that would be in equilibrium with the atmosphere (log PCO2 = -3.5).
1.1e-5 mol C per kilogram water
<number>
Notes: <number>

## Slide 79: Initial Solution 12. Exercise
Calculate the pH and TDIC of a solution in equilibrium with the PCO2 of air (10-3.5) at 25 C.
Calculate the pH and TDIC of a solution in equilibrium with a soil-zone PCO2 of 10-2.0 at 25 C.
Calculate the pH and TDIC of a solution in equilibrium with a soil-zone PCO2 of 10-2.0 at 10 C.
<number>
Notes: <number>
IS.12.
# IS.12. Exercise
SOLUTION 1 Air
-temp 25
pH 7 charge
C 1 CO2(g) -3.5
END
SOLUTION 2 Soil zone
-temp 25
pH 7 charge
C 1 CO2(g) -2.0
END
SOLUTION 2 Soil zone
-temp 10
pH 7 charge
C 1 CO2(g) -2.0
END
IS.12. Answer
pH = 5.66, TDIC = 13 umol/kgw
pH = 4.91, TDIC = 353 umol/kgw
pH = 4.87, TDIC = 552 umol/kgw

## Slide 80: Initial Solution 12. Answers
pH = 5.66, TDIC = 13 umol/kgw
pH = 4.91, TDIC = 353 umol/kgw
pH = 4.87, TDIC = 552 umol/kgw
<number>
Notes: <number>
IS.12.
# IS.12. Exercise
SOLUTION_SPREAD
-units mg/l
Number Temp pH Ca Mg K Na Alkalinity Cl Si S(6) Al
Calcite as CaCO3 Kaolinite
6 17.46 10.31 2.6 3.5 12 330 291 280 19 75 1
END
IS.12. Answer
pH = 8.76
8.3e-8 mol/kgw

## Slide 81: SATURATION INDEX The thermodynamic state of a mineral relative to a solution
<number>
IAP is ion activity product
K is equilibrium constant
Notes: <number>

## Slide 82: SATURATION INDEX
SI < 0, Mineral should dissolve
SI > 0, Mineral should precipitate
SI ~ 0, Mineral reacts fast enough to maintain equilibrium
Maybe
  Kinetics
  Uncertainties
<number>
Notes: <number>

## Slide 83: Rules for Saturation Indices
Mineral cannot dissolve if it is not present
If SI < 0 and mineral is present—the mineral could dissolve, but not precipitate
If SI > 0—the mineral could precipitate, but not dissolve
If SI ~ 0—the mineral could dissolve or precipitate to maintain equilibrium
<number>
Notes: <number>

## Slide 84: Uncertainties in SI: Analytical data
5% uncertainty in element concentration is .02 units in SI.
0.5 pH unit uncertainty is 0.5 units in SI of calcite, 1.0 unit in dolomite
1 pe or pH unit uncertainty is 8 units in SI of FeS for the following equation:
SI(FeS) = log[Fe+3]+log[SO4-2]-8pH-8pe-log K(FeS)
<number>
Notes: <number>

## Slide 85: Uncertainties in SI: Equation
Much smaller uncertainty for SI(FeS) with the following equation :
SI(FeS) = log[Fe+2]+log[HS-]+pH-log K(FeS)
For minerals with redox elements, uncertainties are much smaller if the valence states of the elements in solution are measured.
<number>
Notes: <number>

## Slide 86: Uncertainties in SI: Log K
Apatite from Stumm and Morgan:
Ca5(PO4)3(OH) = 5Ca+2 + 3PO4-3 + OH-
Apatite from Wateq: log K = -55.4
Log Ks especially uncertain for aluminosilicates
<number>
Notes: <number>

## Slide 87: Useful Mineral List Minerals that may react to equilibrium relatively quickly
<number>
Notes: <number>

## Slide 88: Initial Solution 13. Exercise
Examine solution compositions in spreadsheet “solution_spread.xls”.
Calculate saturation indices using phreeqc.dat.
Try out RunPhreeqc macro or copy/paste into PhreeqcI.
What can you infer about the hydrologic setting, mineralogy, and possible reactions for these waters?
<number>
Notes: <number>

## Slide 89: Solution_spread.xls + is13.xls
<number>

## Slide 90: Summary
Aqueous speciation model
  Mole-balance equations—Sum of species containing Ca equals total analyzed Ca
  Aqueous mass-action equations—Activity of products over reactants equal a constant
  Activity coefficient model
    Ion association with individual activity coefficients
    Pitzer specific interaction approach
  SI=log(IAP/K)
<number>
Notes: <number>

## Slide 91: Summary
SOLUTION and SOLUTION _SPREAD
  Units
  pH—ratio of HCO3/CO2
  pe—ratio of oxidized/reduced valence states
  Charge balance
  Phase boundaries
Saturation indices
  Uncertainties
  Useful minerals
Identify potential reactants
<number>
Notes: <number>