## Slide 1: Thursday Afternoon
1D reactive transport with PHEEQC
WEBMOD—Watershed modeling with reactions
Notes: <number>

## Slide 2: 1D Solute Transport
Terms
  Concentration change with time
  Dispersion/diffusion
  Advection
  Reaction
Numerical issues
  Numerical dispersion
  Oscillations

## Slide 3: Field-Scale Examples Concentration Profiles
Analytical and two finite-difference solutions

## Slide 4: PHREEQC Transport Calculations
1
2
3
4
5
6
n
Advection
Dispersion
1
2
3
4
5
6
n
Reaction
1
2
3
4
5
6
n
Notes: <number>

## Slide 5: ADVECTION
Advection
Reactions

## Slide 6: TRANSPORT
Advection
Dispersion
Reactions
Stagnant zones
Heat transport
Multicomponent diffusion
Interlayer diffusion in clay

## Slide 7: Arsenic in the Central Oklahoma Aquifer
Arsenic mostly in confined part of aquifer
Arsenic associated with high pH
Flow:
  Unconfined
  Confined
  Unconfined
<number>

## Slide 8: Geochemical Reactions
Brine initially fills the aquifer
Calcite and dolomite equilibrium
Cation exchange
  2NaX + Ca+2 = CaX2 + 2Na+
  2NaX + Mg+2 = MgX2 + 2Na+
Surface complexation
  Hfo-HAsO4- + OH- = HfoOH + HAsO4-2
<number>

## Slide 9: ADVECTION
Cells are numbered from 1 to N.
Index numbers (of SOLUTION, EQUILIBRIUM_PHASES, etc) are used to define the solution and reactants in each cell
SOLUTION 0 (or N+1) enters the column
Water is “shifted” from one cell to the next

## Slide 10: ADVECTION
Number of cells
Number of shifts
If kinetics—time step

## Slide 11: ADVECTION
Output file
  Cells to print
  Shifts to print
Selected-output file
  Cells to print
  Shifts to print

## Slide 12: Use Range of Numbers

## Slide 13: ADVECTION 1. Exercise Oklahoma transport simulation
We will be plotting results. You can use
  PhreeqcI and Excel (with SELECTED_OUTPUT)
  2. Phreeqc for Windows and USER_GRAPH
  (3. Phreeqcpp in ChartPhreeqc directory also will plot with USER_GRAPH, but is not interactive.)

## Slide 14: ADVECTION 1. Exercise Oklahoma transport simulation
Use the aqueous model and sorption model for arsenic from Dzombak and Morel, 1990 (Cut and paste from PowerPoint)
SURFACE_MASTER_SPECIES
Surf SurfOH
SURFACE_SPECIES
SurfOH = SurfOH
log_k 0.0
SurfOH + H+ = SurfOH2+
log_k 7.29
SurfOH = SurfO- + H+
log_k -8.93
SurfOH + AsO4-3 + 3H+ = SurfH2AsO4 + H2O
log_k 29.31
SurfOH + AsO4-3 + 2H+ = SurfHAsO4- + H2O
log_k 23.51
SurfOH + AsO4-3 = SurfOHAsO4-3
log_k 10.58
SOLUTION_MASTER_SPECIES
As H3AsO4 -1.0 74.9216 74.9216
SOLUTION_SPECIES
#H3AsO4 primary master species
H3AsO4 = H3AsO4
log_k 0.0
#H2AsO4-
H3AsO4 = AsO4-3 + 3H+
log_k -20.7
#HAsO4-2
H+ + AsO4-3 = HAsO4-2
log_k 11.50
#AsO4-3
2H+ + AsO4-3 = H2AsO4-
log_k 18.46

## Slide 15: ADVECTION 1. Exercise—Continued
2. Initial conditions for cells 1-100:
a. Define SOLUTION 1 with the brine composition. (It is possible to cut and paste into PhreeqcI or Phreeqc for Windows).
b. Define EQUILIBRIUM_PHASES 1-100 with 0.1 mol calcite and 1.6 mol dolomite.
c. React solution 1 with equilibirum phases 1 (USE) and SAVE resultomg solution in cells 1-100.
d. Define EXCHANGE 1-100 to have 1 mol of exchanger X and to be in equilibrium with solution 1.
e. Define SURFACE 1-100 to have 0.07 mol of surface complexation sites (Hfo), 600 m^2/g specific surface area, 30 grams of sorbent, and to be in equilibrium with solution 1.

## Slide 16: ADVECTION 1. Exercise—Continued
3. Define infilling solution 0:
a. Define the evaporated rainwater as SOLUTION 0.
b. React solution 0 with EQUILIBRIUM_PHASES 0 that has calcite, dolomite, and pCO2= 10^-1.5. SAVE resulting solution as solution 0.
Notes: <number>
# Exercise T1
SURFACE_MASTER_SPECIES
Surf SurfOH
SURFACE_SPECIES
SurfOH = SurfOH
log_k 0.0
SurfOH + H+ = SurfOH2+
log_k 7.29
SurfOH = SurfO- + H+
log_k -8.93
SurfOH + AsO4-3 + 3H+ = SurfH2AsO4 + H2O
log_k 29.31
SurfOH + AsO4-3 + 2H+ = SurfHAsO4- + H2O
log_k 23.51
SurfOH + AsO4-3 = SurfOHAsO4-3
log_k 10.58
SOLUTION_MASTER_SPECIES
As H3AsO4 -1.0 74.9216 74.9216
SOLUTION_SPECIES
#H3AsO4 primary master species
H3AsO4 = H3AsO4
log_k 0.0
#H2AsO4- 482
H3AsO4 = AsO4-3 + 3H+
log_k -20.7
#HAsO4-2 483
H+ + AsO4-3 = HAsO4-2
log_k 11.50
#AsO4-3 484
2H+ + AsO4-3 = H2AsO4-
log_k 18.46
#
# Define brine
#
SOLUTION_SPREAD
-units mol/kgw
Description Number Temp pH pe Ca Mg Na Cl C S As
O2(g) -0.7 charge uMol/kgw
brine 1 25 5.713 4 0.4655 0.1609 5.402 6.642 0.00396 0.004725 0.05
#
# Define equilibrium_phases 1-10
#
EQUILIBRIUM_PHASES 1-10
Dolomite 0.0 1.6
Calcite 0.0 0.1
END
#
# Equilibrate brine with calcite and dolomite
# Save solutions 1-10
#
USE solution 1
USE equilibrium_phases 1
SAVE solution 1-10
END
#
# Define initial exchange and surface 1-10
#
TITLE Initial exchange and surface
EXCHANGE 1-10
X 1
-equilibrate with solution 1
SURFACE 1-10
-equilibrate with solution 1
Surf 0.07 600 30
END
#
# Define 20xRainwater
#
SOLUTION_SPREAD
-units mmol/kgw
Description Number Temp pH pe Ca Mg Na Cl C S
O2(g) -0.7 charge
20xRainwater 0 25 4.6 4 0.192 0.036 0.123 0.134 0.011 0.235
#
# Equilibrate rainwater with calcite, dolomite, CO2
# Save as solution 0
#
EQUILIBRIUM_PHASES 0
Dolomite 0.0 1.6
Calcite 0.0 0.1
CO2(g) -1.5 10.
SAVE solution 0
END
#
# Advect reacted rainwater through column
# 5 shifts
#
SELECTED_OUTPUT
-reset false
-file t1.sel
-solution
-pH
-alkalinity
-mol NaX CaX2 MgX2
-tot Cl Na Ca Mg
USER_PUNCH
-headings As(ug/L)
-start
10 PUNCH TOT("As")*1e6*74.92
-end
ADVECTION
-cells 10
-shifts 5
-print_frequency 5
-punch_frequency 5
-warnings true
END

## Slide 17: ADVECTION 1. Exercise—Continued
4. Define advection calculation
a. Use ADVECTION data block:
100 cells
75 shifts
print_frequency 75
punch_frequency 75
b. SELECTED_OUTPUT
pH, Cl, Na, Ca, NaX, CaX2 (mol/kgw)
c. USER_PUNCH
As (ug/kgw) (gram formula mass is 75 g/mol)
Notes: <number>
# Exercise T1
SURFACE_MASTER_SPECIES
Surf SurfOH
SURFACE_SPECIES
SurfOH = SurfOH
log_k 0.0
SurfOH + H+ = SurfOH2+
log_k 7.29
SurfOH = SurfO- + H+
log_k -8.93
SurfOH + AsO4-3 + 3H+ = SurfH2AsO4 + H2O
log_k 29.31
SurfOH + AsO4-3 + 2H+ = SurfHAsO4- + H2O
log_k 23.51
SurfOH + AsO4-3 = SurfOHAsO4-3
log_k 10.58
SOLUTION_MASTER_SPECIES
As H3AsO4 -1.0 74.9216 74.9216
SOLUTION_SPECIES
#H3AsO4 primary master species
H3AsO4 = H3AsO4
log_k 0.0
#H2AsO4- 482
H3AsO4 = AsO4-3 + 3H+
log_k -20.7
#HAsO4-2 483
H+ + AsO4-3 = HAsO4-2
log_k 11.50
#AsO4-3 484
2H+ + AsO4-3 = H2AsO4-
log_k 18.46
#
# Define brine
#
SOLUTION_SPREAD
-units mol/kgw
Description Number Temp pH pe Ca Mg Na Cl C S As
O2(g) -0.7 charge uMol/kgw
brine 1 25 5.713 4 0.4655 0.1609 5.402 6.642 0.00396 0.004725 0.05
#
# Define equilibrium_phases 1-10
#
EQUILIBRIUM_PHASES 1-10
Dolomite 0.0 1.6
Calcite 0.0 0.1
END
#
# Equilibrate brine with calcite and dolomite
# Save solutions 1-10
#
USE solution 1
USE equilibrium_phases 1
SAVE solution 1-10
END
#
# Define initial exchange and surface 1-10
#
TITLE Initial exchange and surface
EXCHANGE 1-10
X 1
-equilibrate with solution 1
SURFACE 1-10
-equilibrate with solution 1
Surf 0.07 600 30
END
#
# Define 20xRainwater
#
SOLUTION_SPREAD
-units mmol/kgw
Description Number Temp pH pe Ca Mg Na Cl C S
O2(g) -0.7 charge
20xRainwater 0 25 4.6 4 0.192 0.036 0.123 0.134 0.011 0.235
#
# Equilibrate rainwater with calcite, dolomite, CO2
# Save as solution 0
#
EQUILIBRIUM_PHASES 0
Dolomite 0.0 1.6
Calcite 0.0 0.1
CO2(g) -1.5 10.
SAVE solution 0
END
#
# Advect reacted rainwater through column
# 5 shifts
#
SELECTED_OUTPUT
-reset false
-file t1.sel
-solution
-pH
-alkalinity
-mol NaX CaX2 MgX2
-tot Cl Na Ca Mg
USER_PUNCH
-headings As(ug/L)
-start
10 PUNCH TOT("As")*1e6*74.92
-end
ADVECTION
-cells 10
-shifts 5
-print_frequency 5
-punch_frequency 5
-warnings true
END

## Slide 18: Plot Advection Results
Either
  Import selected output file into Excel
  Or
  Copy input file into Phreeqc for Windows and add USER_GRAPH (next page)

## Slide 19: USER_GRAPH
USER_GRAPH
-headings Cell_number Cl Na Ca NaX CaX2 As(ug/L) pH
-axis_titles "Cell_number“ "Log Concentration" "pH" # x-axis, y-axis, sy-axis
-chart_title "Oklahoma Advection"
-connect_simulations true # true/false
-axis_scale x_axis 0 100 50 10 # min, max, major, minor
-axis_scale y_axis -6 3 1 # min, max, major, minor
-axis_scale sy_axis 0 10 1 # secondary y-axis
-plot_concentration_vs x # distance plot
-start
10 graph_x dist
20 graph_y log10(TOT("Cl")), log10(TOT("Na")), log10(TOT("Ca"))
30 graph_y log10(MOL("NaX")), log10(MOL("CaX2")), log10(TOT("As")*1e6*75)
40 graph_sy -la("H+")
-end

## Slide 20: ADVECTION 1. Questions
Describe the Cl- profile in the column at the end of the simulation.
Describe the pH profile in the column at the end of the simulation.
What is the pH at which arsenic appears to become a problem?
Notes: <number>
A2. Questions
1. Cl is a square wave, low concentrations in first 75 cells, high concentrations in last 25 cells.
2. pH ~7.5 in first cell, pH is > 9 for 50 cells, decreases to < 5.5 by cell 70, up to constant 5.6.
3. Arsenic > 10 ug/L when pH is above 8.5.
Choride is a square-wave front because only advection is simulated. The front has moved 5 cells because there have been 5 shifts.
pH decreases from pH 9 to pH 6 from cell 2 to cell 6.
Cell 3 has pH 8.5, but little arsenic. Cell 2 has pH 9 and 100 ug/L As. So greater than pH 8.5.

## Slide 21: ADVECTION 1. Answers
Ca, Mg exchange for Na
Calcite, dolomite dissolve
pH > 9
As > 100 ug/L
Notes: <number>

## Slide 22: Phreeqc For Windows

## Slide 23: PHREEQCPP

## Slide 24: ADVECTION 1. Answers
1. Cl is a square wave, low concentrations in first 75 cells, high concentrations in last 25 cells.
2. pH ~7.5 in first cell, pH is > 9 for 50 cells, decreases to < 5.5 by cell 70, up to constant 5.6.
3. Arsenic > 10 ug/L when pH is above 8.5.

## Slide 25: TRANSPORT
Cell lengths
Velocity=length/time step!
Dispersivities

## Slide 26: TRANSPORT
Boundary conditions
Flow direction
Diffusion coefficient
Heat

## Slide 27: TRANSPORT
Stagnant cells/dual porosity
-One stagnant cell
-Multiple stagnant cells

## Slide 28: TRANSPORT—Charge-Balanced Diffusion
TRANSPORT
-multi_d true 1e-9 0.3 0.05 1.0
SOLUTION_SPECIES
H+ = H+
log_k 0.0
-gamma 9.0 0.0
-dw 9.31e-9
Multicomponent diffusion—true
Default tracer diffusion coefficient—1e-9 m2/s
Porosity—0.3
Minimum porosity—0.05
(Diffusion stops when the porosity reaches the porosity limit)
Exponent of porosity (n) –1.0.
(Effective diffusion coefficient–De = Dw * porosity^n)
-dw is tracer diffusion coefficient in SOLUTION_SPECIES