## Slide 1: Geochemistry Modeling Workshop, March 2011
Pierre Glynn
David Parkhurst
Ray Johnson
Participants

## Slide 2: FIELD WORK
Water
  Inorganic constituents
  Nutrients
  Organic constituents
  Gases: CFC, Noble
  Stable isotopes: D, 18O, 13C, 34S, 87Sr
  Other stable isotopes : N, Ca, B, Pb, Fe
  Radioisotopes: T/He, 14C
Rocks
  X-ray
  SEM, optical microscopy
  Isotopic analysis
  Whole rock
  Selective extractions

## Slide 3: PHASES OF GEOCHEMICAL MODELING—TRENDS
Maps
Stiff diagrams
Plots of concentration against Cl, pH
Saturation indices
Time series
Hydrology

## Slide 4: PHASES OF GEOCHEMICAL MODELING—INVERSE MODELING
Need to know sequence of water chemistry
Hydrology
Mineralogy
Deduce chemical reactions affecting major elements in water and rocks
Not effective for trace elements

## Slide 5: INVERSE MODELING—Estuarine Pore Water
Solution fractions: Minimum Maximum
Seawater 4.160e-001 0.000e+000 0.000e+000
Pore water 1.000e+000 0.000e+000 0.000e+000
Phase mole transfers: Minimum Maximum
Pyrite -3.803e-003 0.000e+000 0.000e+000 FeS2
Fe(OH)3(a) 3.808e-003 0.000e+000 0.000e+000 Fe(OH)3
H2O(g) 3.240e+001 0.000e+000 0.000e+000 H2O
Calcite 1.049e-003 0.000e+000 0.000e+000 CaCO3
Organic carbon 2.116e-002 0.000e+000 0.000e+000 CH2O
CaX2 -1.019e-003 0.000e+000 0.000e+000 CaX2
NaX 2.039e-003 0.000e+000 0.000e+000 NaX
Notes: <number>
# IS.2 Seawater
SOLUTION 10
temp 25
pH 7
pe 4
redox pe
units ppm
density 1
Ca 412.3
Mg 1291.8
Na 10768
K 399.1
Fe 0.002
Alkalinity 141.682 as HCO3
Cl 19353
S(6) 2712
-water 1 # kg
PHASES
PHASES
OC
CH2O = 0.5 CO2 + 0.5CH4
log_k 0
SOLUTION_SPREAD
-units mmol/l
Description Number Temp pH O(0) Ca Mg Na K Alkalinity Cl S(6) Fe(2) S(-2) N(-3)
meq/l
V6, 1 cm 1 20 7.23 0 4.7 25.3 216 5.9 6.4 257 10 0.009 1 0.35
V6, 5 cm 5 20 7.45 0 4.4 22.2 190 5.3 24 223 0.5 0.005 3.4 2.27
INVERSE_MODELING 1
-solutions 10 5
-uncertainty 0.1
-phases
pyrite
Fe(OH)3(a)
H2O(g)
Calcite
OC
CaX2
KX
NaX
-balances
Alkalinity 0.05 0.05
C 0.05 0.05
Ca 0.05 0.05
Cl 0.05 0.05
Fe 0.05 0.05
Mg 0.05 0.05
Na 0.05 0.05
S 0.05 0.05
-tolerance 1e-010
-mineral_water true

## Slide 6: PHASES OF GEOCHEMICAL MODELING—FORWARD MODELING
Batch reaction calculations
Equilibrium
  Minerals and Gases
  Exchange
  Surface
Nonequilibrium
  Irreversible reactants
  Kinetics

## Slide 7: FORWARD MODELING—TRENDS IN CARBONATE GW
Notes: <number>
solution
end
use solution 1
reaction
CO2 1
10 mmol in 100 steps
equilibrium_phases
Calcite
Dolomite
selected_output
-file pco2-gw.sel
-reset false
-rxn
user_punch
-heading pCO2 Ca Mg C pH
10 punch si("CO2(g)")
20 punch tot("Ca")*1000, tot("Mg")*1000, tot("C")*1000, -la("H+")
END

## Slide 8: 1D Reactive-Transport Modeling
Must know flow
  Direction
  Rate
Must know reactions

## Slide 9: 1D REACTIVE TRANSPORT—Carbonates, ion exchange, surface complation
Notes: <number>
TITLE Example 14.--Transport with equilibrium_phases, exchange, and surface reactions
***********
PLEASE NOTE: This problem requires database file wateq4f.dat!
Arsenic data of Archer and Nordstrom (2002) included in
wateq4f.dat (PHREEQC Version 2.8).
Results differ from WRIR 99-4259 because of revised data.
***********
SURFACE_SPECIES
Hfo_wOH + Mg+2 = Hfo_wOMg+ + H+
log_k -15.
Hfo_wOH + Ca+2 = Hfo_wOCa+ + H+
log_k -15.
SOLUTION 1 Brine
pH 5.713
pe 4.0 O2(g) -0.7
temp 25.
units mol/kgw
Ca .4655
Mg .1609
Na 5.402
Cl 6.642 charge
C .00396
S .004725
As .05 umol/kgw
END
USE solution 1
EQUILIBRIUM_PHASES 1
Dolomite 0.0 1.6
Calcite 0.0 0.1
SAVE solution 1
# prints initial condition to the selected-output file
SELECTED_OUTPUT
-file ex14.sel
-reset false
-step
USER_PUNCH
-head m_Ca m_Mg m_Na umol_As pH
10 PUNCH TOT("Ca"), TOT("Mg"), TOT("Na"), TOT("As")*1e6, -LA("H+")
END
PRINT
# skips print of initial exchange and initial surface to the selected-output file
-selected_out false
EXCHANGE 1
-equil with solution 1
X 1.0
SURFACE 1
-equil solution 1
# assumes 1/10 of iron is HFO
Hfo_w 0.07 600. 30.
END
SOLUTION 0 20 x precipitation
pH 4.6
pe 4.0 O2(g) -0.7
temp 25.
units mmol/kgw
Ca .191625
Mg .035797
Na .122668
Cl .133704
C .01096
S .235153 charge
EQUILIBRIUM_PHASES 0
Dolomite 0.0 1.6
Calcite 0.0 0.1
CO2(g) -1.5 10.
SAVE solution 0
END
PRINT
-selected_out true
ADVECTION
-cells 1
-shifts 200
-print_frequency 20
END

## Slide 10: 3D REACTIVE-TRANSPORT MODELING
Ground-water flow model
Boundary condition water compositions
Initial conditions
Geochemical reactions

## Slide 11: 3D REACTIVE-TRANSPORT-- PO4 at Cape Cod Sewage Plume

## Slide 12: Geochemical Tools
Saturation Indices—PhreeqcI, NETPATH
Inverse modeling—PhreeqcI, NETPATH (isotope fractionation)
Forward modeling—PhreeqcI
1D Reactive-transport modeling—PhreeqcI, PHAST
3D Reacive-transport modeling--PHAST

## Slide 13: Presentations
Background
What question are you trying to answer?
Do you need geochemical modeling?
Which types of modeling are appropriate?
Do you have the necessary data?